## Slide 1: Chapter 6: Food Preservation through Water Removal
Dr. Mohammed Sabbah
Page 332
Book: Food Processing Technology
- Water Activity - Drying Technology

## Slide 2: Water Activity
Page 70 In Food processing technology

## Slide 3
Food preservation has as its goal the extension of shelf life of foods to allow storage and convenient distribution.
The most dangerous source of limitation of shelf life is due to the activity of microorganisms. The first aim of food preservation is therefore to limitation the danger of spoilage due to microbes.
These processes include concentration, dehydration, and freezing. Concentration and dehydration reduce availability of water by reducing the total water content.
1. Introduction

## Slide 4
Freezing results in crystallization of most of the water and consequently in a much reduced water content in the unfrozen portion of the food. Other preservation processes are based on adding solutes, such as sugars or salt, which reduces water availability.
In addition to controlling microbial Activity Water has a profound influence on the physical and chemical processes which influence shelf life. Water management is therefore a key aspect of food technology,

## Slide 5
Transport media (nutrients and metabolism wastes),
Reactant, reaction media, stabilizer (biopolymer, temperature),
Facilitate to dynamic characteristics of macromolecule (i.e., enzyme).
2. Role of Water in Organisms
H2O

## Slide 6
Affect the freshness of foods.
Affect the storage periods of foods.
Affect the quality of foods.
Role of Water in Foods

## Slide 7
Water Activity
Correct Definition: Water activity is a measure of the energy status of the water in a system.
Old Defination : Water activity (aw) is amount of water available for microbial (bacteria, yeast and mold) growth. Water activity is based on a scale of 0 to 1.0 with pure water having a water activity of 1.00. Usually products that contain lower percent moisture have lower water activities.
Water Activity: is the water vapor pressure of the amount of water in a material relative to the water vapor pressure of pure water expressed as a ratio.
3. Water Activity Defined

## Slide 8
For example, if the vapor pressure of the water in a material is 70% of pure water (or the saturated material) the aw will be 0.7.
aw is measured by placing the material in a sealed chamber, allowing the air in the chamber to reach moisture equilibrium with the material, and then measuring the relative humidity and multiplying by 100 to get the ratio.

## Slide 9
  P
  aw = ------
  pº
  ERH
  aw = ------
  100
  ERH = Equilibrum Relative Humidity
p = partial pressure(الضغط الجزئي) of water in food at a given temperature and
pº= vapor pressure of water at the same temperature.
Aw (Activity of Water/ Water Activity)

## Slide 10
Moisture Content or Water content
Water content or moisture content is the quantity of water contained in a material.
An extensive property خاصية واسعة النطاق that depends on the amount of material.
Water activity
Water activity (aw) is amount of water available for microbial (bacteria, yeast and mold) growth(Qualitative).
Intensive property that does not depend on the amount of material.
4. Difference between aw and water content

## Slide 11
5. aw in the Food Industry
5.1 Growth of Micro-Organisms
Water activity indicates the amount of water in the total water content which is available to micro-organisms. Each species of micro-organism (bacteria, yeast and mold) has its own minimum aw value below which growth is no longer possible.
Most bacteria do not grow below water activity of 0.85, and no bacterial pathogens are known to grow below than water activity, even when the other environmental parameters (e.g., pH, temperature, nutrient content) are optimal.
Growth and toxin production by all types of Clostridium botulinum: 0.94
Anaerobic growth of Staphylococcus aureus 0.91
Aerobic growth of Staphylococcus auerus 0.85
Production of toxins by molds 0.80

## Slide 12
Effect of water activity on microbial, enzymic and chemical changes to foods.

## Slide 14
5.2 Chemical Stability
Water activity control is an important factor for the chemical stability of foods. Most foodstuffs contain carbohydrates and proteins and are therefore subject to non-enzymatic browning reactions (Maillard reaction). The Maillard reaction gets stronger at increasing aw values and reaches its peak at aw = 0.6 to 0.7 with further increase of aw this reaction gets rapidly weaker.
5. 3. Enzymatic Stability
Most enzymatic reactions are slowed down at aw values below 0.8. Some of these reactions occur even at very low aw values.
5.4. Drying Process
Warm air increases the water-vapour pressure generated by the product to be dried by increasing its temperature.

## Slide 15
Chemical/Biochemical Stability
Water activity effect on reaction rate
  Most reaction rates increase with increasing water activity
  Most rates correlate better with aw than moisture content
  Water may act as a:
    solvent
    reactant
    change the mobility of reactants (viscosity)

## Slide 16
Water activity and microbial growth
  Most bacteria can’t grow below aw = 0.85
  Most yeasts & molds can’t grow below aw = 0.65
Relative growth or reaction rate

## Slide 17
Fig. 3. Moisture sorption isotherm. Food with low moisture content.
Sorption hysteresis
A sorption isotherm (hysteresis): (also adsorption isotherm) describes the equilibrium of the sorption of a material at a surface at constant temperature.

## Slide 19
6. Reducing water activity
Drying or concentrating: remove water from the food
drying with heat - evaporation
freeze-drying – sublimation
concentration by evaporation
concentration by filtration
Add solutes to the food: Bind “free” water:
Sugar, salt, proteins, and others

## Slide 20
Typical water activity of some foods
0.95 – fruits, vegetables, meat, fish, milk
0.91 – some cheeses, ham
0.87 – salami, pepperoni, dry cheeses, margarine,
0.80 – fruit juice concentrates, sweetened condensed milk, syrups,
flour, rice, high sugar cakes
0.75 – jam, marmalade
0.65 – oatmeal, fudge, marshmallows, jelly, molasses, sugar, nuts
0.60 – dried fruits, honey
0.50 – dried pasta, dried spices
0.30 – cookies, crackers
0.03 – dry milk, dehydrated soups, corn flakes
Aw – examples

## Slide 22
Water Activity Definition
Experiment - Place together in a sealed container Component A & Component B
Which way does water move?
25% Moisture
52% Moisture
A
B

## Slide 23
Water Activity Definition
Equilibrium Conditions
aw Component A = aw Component B = aw air
At equilibrium the energy status (chemical potentials) are the same and thus no net exchange of water.

## Slide 24
7. Methods of measured water activity
Experiment 1.1 : Determination of Water Activity Curve for Nonfat Dry Milk
Nonfat dry milk samples: Your group will evaluate one sample.
2.Saturated Salt Solutions: You will use eight different saturated salt solutions to your water activity curve. Table 1 shows the expected water activity and the recipe to prepare the solutions.
3. Aluminum weighing dishes
4. Mason jars with wire racks

## Slide 25
Measurement the water activity

## Slide 26
HygroPalm HP23-A / HP23-AW-A Hand-Held Indicator User Guide

## Slide 28
Drying Technology

## Slide 29: Drying Technology
Dehydration (or drying) is defined as ‘the application of heat under controlled conditions to remove the majority of the water normally present in a food by evaporation’ (or in the case of freeze drying by sublimation).
How Drying Preserves
The main purpose of dehydration is to extend the shelf life of foods by a reduction in water activity. This inhibits microbial growth and enzyme activity, but the processing temperature is usually insufficient to cause their inactivation.

## Slide 30
Drying causes deterioration of both the eating quality and the nutritional value of the food.
Examples of commercially important dried foods are coffee, milk, raisins, and other fruits, pasta, flours, beans, nuts, breakfast cereals, tea and spices.

## Slide 31
There are a large number of factors that control the rate at which foods dry, which can be grouped into the following categories:
those related to the processing conditions
those related to the nature of the food
those related to the drier design.

## Slide 32
Hot-air drying
Kiln dryer
Tray dryer
Tunnel dryer
Conveyor dryer
Bin dryer
Fluidized bed dryer
Pneumatic dryer
Rotary dryer
Spray dryer
Drying by contact with a heated surface
Drum dryer
Vacuum shelf dryer
Vacuum band dryer
Drying methods

## Slide 33
Drying by the application of energy from radiation, microwave or dielectric source.
Radiant heating drying
Continuous infra-red dryer
Microwave and dielectric heating drying
Freeze drying (sublimation drying, lyophilisation)
Batch freeze-dryers
Multicabinet freeze-dryers
Tunnel freeze-dryers

## Slide 34: 2.1.Drying using heated air
There are three inter-related factors that control the capacity of air to remove moisture from a food:
1. the amount of water vapor already carried by the air
2. the air temperature
3. the amount of air that passes over the food.
The amount of water vapor in air is expressed as either absolute humidity or relative humidity (RH) (in percent).
Psychrometric is the study of inter-related properties of air–water vapor systems.

## Slide 35: 2.2. Mechanism of drying
The third factor that controls the rate of drying, in addition to air temperature and humidity, is the air velocity. When hot air is blown over a wet food, water vapor diffuses through a boundary film of air surrounding the food and is carried away by the moving air.
A water vapour pressure gradient is established from the moist interior of the food to the dry air. This gradient provides the ‘driving force’ for water removal from the food.

## Slide 37: 2.3. Follow: factors affecting on drying
The composition and structure of the food has an influence on the mechanism of moisture removal. For example, the orientation of fibres in vegetables (e.g. celery) and protein strands in meat allow more rapid moisture movement along their length than across the structure.
The amount of food placed into a drier in relation to its capacity (in a given drier, faster drying is achieved with smaller quantities of food).

## Slide 38
Fig .1 Kiln dryer
1. Kiln dryer
2.4. Hot-air drying

## Slide 39
Rotary dryers potentially represent the oldest continuous and the most common high volume dryer used in industry, and it has evolved more adaptations of the technology than any other dryer classification.
All rotary dryers have the feed materials passing through a rotating cylinder termed a drum. It is a cylindrical shell usually constructed from steel plates, slightly inclined, typically 0.3-5 m in diameter, 5-90 m in length and rotating at 1-5 rpm.
2. Rotary Dryers

## Slide 40
Figure. 3. Rotary Dryers

## Slide 41
Fig. 2 Tray dryer
3. Tray dryer

## Slide 42
Fig.3 Tunnel dryer
4. Tunnel dryer

## Slide 43
Fig. 4 Conveyor dryer
5. Conveyor dryer

## Slide 44
The pneumatic or ‘flash’ dryer is used with products that dry rapidly owing to the easy removal of free moisture or where any required diffusion to the surface occurs readily. Drying takes place in a matter of seconds. Wet material is mixed with a stream of heated air (or other gas), which conveys it through a drying duct where high heat and mass transfer rates rapidly dry the product.
6. Flash Dryer
There are several types of dispersion dryers, namely flash dryers, fluidized bed dryers, and spray dryers.

## Slide 45
Fig. 5 Pneumatic dryer system dryer

## Slide 46
Spray drying has been one of the most energy-consuming drying processes, yet it remains one that is essential to the production of dairy and food product powders. Basically, spray drying is accomplished by atomizing feed liquid into a drying chamber, where the small droplets are subjected to a stream of hot air and converted to powder particles.
The advantage of spray dryer
Solutions, suspensions, slurries and pastes, which can be pumped, can be dried on spray dryers. The advantage of spray dryer is rapid and non-contact drying.
Much higher initial temperature of drying medium can be used. High evaporation rates and thermal efficiencies are achieved.
It can be quickly started and shut down.
7- Spray Dryers

## Slide 47
Atomization is a key part of spray drying, since it controls in large measure particle size distribution as well as particle flight patterns in the chamber. Three types of atomizers are employed:
1- Centrifugal atomizers: Droplets in the range of 1 to 600 µm can be produced.
2-Pressure nozzle atomizers : The range of achievable droplet size is reported as 10 to 600 µm.
3- Two fluid nozzles: produce a spray by using a second fluid, such as compressed air or steam, to atomize the feed. The range of droplet sizes produced in these atomizers is 6 to 600 µm. In these atomizers the droplet size may be related to the volumetric flow rates of the feed fluid and the atomizing fluid (usually air) .

## Slide 49
Typical operating parameters reported for spray drying of dairy products are:
Entering moisture content is 48 to 85%.
Exit moisture content is 2.5 to 5%.
Inlet air temperature is 150 to 220 ºC .
Outlet temperature of air is 50 to 100 ºC.
The factor controlling the conditions adapted for drying is the quality of the product.

## Slide 50
Figure. 5. Spray drying

## Slide 51
Fig.6: Various types of dryers

## Slide 52: 2.2 Drying using heated surfaces
Heat is conducted from the hot surface, through the food, and moisture is evaporated from the exposed surface. The main resistance to heat transfer is the thermal conductivity of the food
Knowledge of the rheological properties of the food is therefore necessary to determine the thickness of the layer and the way in which it is applied to the heated surface

## Slide 53
Vacuum shelf dryer
Vacuum band dryer
Drum dryer

## Slide 54
Effect on foods
All products undergo changes during drying and storage that reduce their quality compared to the fresh material and the aim of improved drying technologies is to minimise these changes while maximising process efficiency.
The main changes to dried foods are to the texture and loss of flavour or aroma, but changes in colour and nutritional value are also significant in some foods

## Slide 55
Drying pieces of meat is not common in many countries owing to the severe changes in texture compared with other methods of preservation. These are caused by aggregation and denaturation of proteins and a loss of Water-Holding Capacity (WHC), which leads to toughening of muscle tissue.
In general, rapid drying and high temperatures cause greater changes to the texture of foods than do moderate rates of drying and lower temperatures.
As water is removed during drying, solutes move from the interior of the food to the surface. The mechanism and rate of movement are specific for each solute and depend on the type of food and the drying conditions used.
1. Texture

## Slide 56
Evaporation of water causes concentration of solutes at the surface. High air temperatures (particularly with fruits, fish and meats), cause complex chemical and physical changes to solutes at the surface, and the formation of a hard impermeable skin. This is termed case hardening and it reduces the rate of drying to produce a food with a dry surface and a moist
In principle, water-holding capacity (WHC) is defined as the ability of meat to hold all or part of its own water.

## Slide 57
2. Flavour and aroma
Heat not only vaporises water during drying but also causes loss of volatile components from the food and as a result most dried foods have less flavour than the original material.
The extent of volatile loss depends on the temperature and moisture content of the food and on the vapour pressure of the volatiles and their solubility in water vapour.
Volatiles which have a high relative volatility and diffusivity are lost at an early stage in drying. Foods that have a high economic value due to their characteristic flavours (for example herbs and spices) are dried at low temperatures.

## Slide 58
Flavour changes, due to oxidative or hydrolytic enzymes are prevented in fruits by the use of sulphur dioxide, ascorbic acid or citric acid, by pasteurisation of milk or fruit juices and by blanching of vegetables. Other methods which are used to retain flavours in dried foods include:
1- recovery of volatiles and their return to the product during drying.
2 -mixing recovered volatiles with flavour fixing compounds, which are then granulated and added back to the dried product (for example dried meat powders)
3- addition of enzymes, or activation of naturally occurring enzymes, to produce flavours from flavour precursors in the food (for example onion and garlic are dried under conditions that protect the enzymes that release characteristic flavours).
Notes: is a chemical reaction during which molecules of water (H2O) are split into hydrogen cations (H+, conventionally referred to as protons) and hydroxide anions (OH−) in the process of a chemical mechanism. It is the type of reaction that is used to break down certain polymers, especially those made by condensation polymerization. Such polymer degradation is usually catalysed by either acid, e.g., concentrated sulfuric acid (H2SO4), or alkali, e.g., sodium hydroxide (NaOH).

## Slide 59: 3. Colour
There are a number of causes of colour loss or change in dried foods; drying changes the surface characteristics of a food and hence alters its reflectivity and colour. In fruits and vegetables, chemical changes to carotenoid and chlorophyll pigments are caused by heat and oxidation during drying and residual polyphenoloxidase enzyme activity causes browning during storage.
The rate of Maillard browning in stored milk and fruit products depends on the water activity of the food and the temperature of storage. The rate of darkening increases markedly at high drying temperatures, when the moisture content of the product exceeds 4–5%, and at storage temperatures above 38ºC

## Slide 60: 4. Nutritional value
Large differences in reported data on the nutritional value of dried foods are due to wide variations in the preparation procedures, the drying temperature, time, and the storage conditions. In fruits and vegetables, losses during preparation usually exceed those caused by the drying operation.
Vitamins have different solubilities in water and as drying proceeds, some (for example riboflavin) become supersaturated and precipitate from solution, so losses are small .
Others, for example ascorbic acid, are soluble until the moisture content of the food falls to very low levels and these react with solutes at higher rates as drying proceeds. Vitamin C is also sensitive to heat and oxidation and short drying times, low temperatures, low moisture and oxygen levels during storage are therefore necessary to avoid large losses.

## Slide 61: Vitamin losses in selected dried foods

## Slide 62: Rehydration
Water that is removed from a food during dehydration cannot be replaced in the same way when the food is rehydrated (that is, rehydration is not the reverse of drying);
loss of cellular osmotic pressure,
changes in cell membrane permeability,
solute migration,
crystallisation of polysaccharides and
coagulation of cellular proteins all contribute to texture changes and volatile losses and are each irreversible