## Slide 1
Digital Communications
Other forms of Pulse Modulation
DM, DSM, DPCM, ADPCM, LP,…
2

## Slide 2: 1) Delta Modulation
PCM has certain limitations So, we use other forms like;
DM (Delta Modulation)
  An incoming message signal is oversampled to purposely increase the correlation between adjacent samples of the signal
  The difference between the input signal and its approximation is quantized into only two levels - corresponding to positive and negative differences

## Slide 3: Fig.5.14
Back
Next

## Slide 4: System Details for DM
Comparator
  Computes the difference between its two inputs
Quantizer
  Consists of a hard limiter with an input-output characteristic that is a scaled version of the signum function
Accumulator
  Operates on the quantizer output so as to produce an approximation to the message signal.

## Slide 5: Fig. DM Tx & Rx
Back
Next

## Slide 6: Quantization Errors
  Slope-overload distortion
    The step size is too small for the staircase approximation to follow a steep segment of the original message signal
    The result that the approximation signal falls behind the message signal
  Granular noise
    When the step size is too large relative to the local slope characteristic of the original message signal
    The staircase approximation to hunt around a relatively flat segment of the message signal.
Fig. 5.16

## Slide 7: Fig.5.16
Back
Next
Solution:

## Slide 8
In order for the sequence of samples {mq[n]} to increase as fast as the input sequence of samples {mq[n]} in a region of maximum slope of m(t), the following condition must be satisfied,
- Otherwise; Delta is too small for the stair case approximation.
- granular noise occurs when Delta is too large & it is similar to quantization noise in PCM .
  - We need large Delta to solve slope overload distortion
  - We need small Delta to solve granular distortion
The Solution is Adaptive Delta Size (ADM)

## Slide 9: 2) Delta-Sigma Modulation (Sigma-delta modulation)
In DM noise result in an accumulative error in the demodulated signal
This draw back can be over come by integrating the message signal prior to DM
SDM is a delta modulation system that incorporates integration at its input
Benefit of the integration
  The low-frequency content of the input signal is pre-emphasized
  Correlation between adjacent samples of the delta modulator input is increased
  Design of the receiver is simplified

## Slide 10: Fig.5.17
Back
Next

## Slide 11: 3) Differential Pulse Code Modulation (DPCM)
Often voice and video signals do not change much from one sample to the next.
Such signals has energy concentrated in lower frequency.
Sampling faster than necessary generates redundant information.
Hence, we Can save bandwidth by not sending all samples, but:
  - Send true samples occasionally. - In between, send only the change from previous value. - This change is sent using a fewer number of bits than true samples.
Examples (CCITT standards) (CCITT, now ITU-T) * 32 k bits / s (4-bit quantization and 8 k samples /s) for 3.2kHz
* 64 k bits / s (4-bit quantization and 16 k samples /s) for 7 kHz

## Slide 12: Differential Pulse-Code Modulation- DPCM
Prediction
If we know the past behavior of a signal up to a certain point in time, it is possible to make some inference (prediction) about its future values
Tapped-delay-line filter (discrete-time filter)
  A simple and yet effective approach to implement the prediction filter
  With the basic delay set equal to the sampling period
The quantizer output may be expressed as
Fig. 5.19

## Slide 13: Fig.5.18
Back
Next
For slowly varying signals, a future sample can be predicted from past samples.

## Slide 14
  Comparing the DPCM with DM system,
    The use of a one-bit (two-level) quantizer in the DM system
    Replacement of the prediction filter in the DPCM by a single delay element in DM.
  Noise is concerned
    DPCM, like DM, is subject to slope-overload distortion whenever the input signal changes too rapidly for the prediction filter to track it
    Like PCM, DPCM suffers from quantization noise

## Slide 15
Differential Pulse Code Modulation (DPCM)
fs >>fN highly correlated samples .
highly correlated
samples
PCM
Encoded signal with redundant information
Symbols that are not essential to the transmission are generated as a result of PCM encoding
Removing the redundancy before encoding more efficient coded signal
DPCM Depends on Linear Prediction (we send (we code)) only the difference between samples not like PCM nor like DM).
m[n]=
^

## Slide 16
LPF
SAMPLER
ENCODER
QUANTIZER
REGENE
DECODER
LPF
reconst
Distination
m(t)
PCM
Applied to channel input
PCM
Quantizer
Encoder
decoder
Prediction
filter
prediction
input
Sampled input m[n]
DPCM
Wave
Fig. DPCM Tx
Fig. DPCM Rx
+
+
+
+
+
-
eq[n]
e[n]
m[n]
^
mq[n]
mq[n]=m[n]+eq[n]
^
eq[n]=e[n]+q[n]

## Slide 17
e[n] = m[n] – m[n]
eq[n] = e[n] + q[n]
mq[n] = m[n] + eq[n]
= m[m] + e[n]+ q[n]
mq[n] = m[n] + q[n] mq[n] is the quantize version of the input signal .
q[n] can be +
^
^
^
-
The prediction filter in the Tx & Rx operates on the same sequence of sample, mq[n]. So we have a feedback path added to the quantizer in the Tx.

## Slide 18
The variance of the prediction error e[n] is smaller than the variance of the message signal m[n], so we have a smaller quantization error.
m[n] mq [n]
OR e[n] eq [n].
Q
Q
m[n]
e[n]
eq [n]
1- Quantizer (DPCM)
OR
2- One bit Q (DM)
Encoder
Prediction filter -DPCM
OR
Z^-1 ( DM)
mq [n]
+
-
+
+
mh[n] (DPCM)
OR
mq[n-1] (DM)
DPCM
OR
DM
Comparing
DM with DPCM

## Slide 19
DM uses one –bit (two-level) quantizer.
DM prediction filter is a single delay element (zero prediction order).
DM and DPCM Transmitters use feedback but PCM does not.
DM and DPCM are subject to slope-over load distortion .
PCM and DPCM suffers from quantization noise.
So, DM is a special case of DPCM BUT

## Slide 20
Adaptive Differential Pulse Code Modulation (ADPCM)
Standard PCM 64 kb/s HENCE, large B.W is required .
To reduce bit rate, we can use coding :
1) Remove redundancies from the signal (speech) as far as possible.
2) Assign the available bits to code the non redundant parts of the signal in a perceptually efficient manner .
Reducing bit rate increasing the complexity .
ADPCM 32kb/s adaptive quantization .
adaptive prediction.

## Slide 21
Inappropriate step size δ creates noise. Make delta (δ or D) adaptive. number of successive 1’s or 0’s step size 1 δ 2 δ 3 2δ 4 4δ … ...
4) Adaptive Delta Modulation

## Slide 22: ADM Block Diagram.

## Slide 23
Computer Experiment: Adaptive Delta Modulation
In DM ,
1) If successive errors are of opposite polarity then DM is in the granular mode, so we may reduce the step size.
2) if successive errors are of the same polarity then, DM is in the slop – over load mode, so we may increase the step size.
In ADM
For (1) above, we may increase or decrease the step size D to be 2D, 3D, 4D,…
OR
D  Dmin
i.e., delta adaptation
NEED the equation ??

## Slide 24: More techniques to be discussed later
Liner Prediction
Liner Adaptive Prediction
Adaptive Differential Pulse Code Modulation
Fig. 5.20

## Slide 25: Speech Coding
Waveform coders: output approximates original voice signal. * PCM, DPCM, DM, CVSD (24 – 64 k bits/s) - Vocoder: parameterize voice signals based on speech models * CELP, VSELP (2 -16 k bits/s)

## Slide 26: Comparing Encoding Techniques to speech signal (fs=8kHz.)

## Slide 27
BASIS OF COMPARISON | PCM | DM | ADM | DPCM
Number of Bits | It can use 4,8 or 16 bits per sample. | It uses one bit for one sample. | It uses only one bit for one sample. | Bits can be more than one but are less than PCM.
Levels And Step Size | The number of levels depends on number of bits. Level size is fixed. | Step size is kept fixed and cannot be varied. | Step size varies according to the signal variation. | Number of levels is fixed.
Quantization Error & Distortion | Quantization error depends on the number of levels. | Slope-overload distortion is present. | Quantization noise is present but no other errors. | Slope overload distortion and quantization noise is present.
Bandwidth | Highest bandwidth is required since the number of bits is high. | Lowest bandwidth is required. | Lowest bandwidth is required. | Bandwidth required is less than PCM.
Feedback | There is no feedback in transmitter or receiver. | Feedback exists in the transmitter. | Feedback exists in the transmitter. | Feedback exists in the transmitter.
Complexity | Complex system to implement. | Simple to implement | Simple to implement. | Simple to implement.
Table: PCM Vs DM Vs ADM Vs DPCM

## Slide 28: Time Division Multiplexing - TDM

## Slide 29: Time Division Multiplexing - TDM
Time-division Multiplexing
  Enables the joint utilization of a common communication channel by a plurality of independent message sources without mutual interference among them
  Highly sensitive to dispersion in the common channel – a non-constant magnitude response of the channel and a nonlinear phase response.
Synchronization
  Keep the same time as a distant standard clock at the transmitter
  One possible procedure to synchronize the transmitter and receiver clocks is to set aside a code element or pulse at the end of a frame and to transmit this pulse every other frame only

## Slide 30: Concept (TDM)
1. Restricting each input by low-pass anti-aliasing filter
2. Commutator – takes sample from each input message (fs > 2W); interleave samples in a frame Ts;
3. Pulse modulator – transformation for transmission over common channel
4. Pulse demodulator
5. Decommutator – synchronized with the commutator

## Slide 31: Synchronization
TDM - Easy to add and drop sources
Pulses duration considerations
  time interval limited by the sampling rate (reciprocal)
  more users – shorter pulses – difficult to generate; highly influenced by impairments
  upper limit of number of independent sources
Transmitter-receiver clock sync – very important – two local clocks
  separate code element or pulse at the end of a frame
  orderly procedure for detecting sync pulses – searching procedure

## Slide 32
Time interleaving of samples from different sources to be transmitted over a single communication channel.
Time Division Multiplexing

## Slide 33
1)The commutator
1-Takes a narrow sample of each of the N signals at a rate fs>2W.
2-Sequentially interleave these N samples inside the sampling interval Ts.
TDM Bandwidth expansion factor N.
2) Pulse modulator
Transfers the multiplexed signal into a form suitable for transmission over the communication channel.
3) Pulse demodulator +Decommulator (reverse process at the receiver)
Frame Ts
S11 S21 S31 S41 S51 S12 S22 S32 S42 S52

## Slide 34: T1 TDM Format for One Frame.
(8000 samples / s)

## Slide 35
For PCM. System :
As the number of signals to be TDM increases, the duration of a codeword representing a single sample is reduced. Hence pulse duration is reduced. So it is more difficult for generating or transmitting.
For short pulses, we have more noise in the Tx media .
So, we have a restricted number of signals to be TDM .
The time operation at the Rx follow closely the time operation at the Tx. (except for transmission time…)
How to synchronize the Tx + Rx?
Set a pulse at the end of a frame and transmit this pulse every other frame only.
Synchronization

## Slide 36: Example: The T1 System - (Compare it to E1 system?)
24 voice channels; separate pairs of wires; regeneration every 2 km; basic to the North American Digital Switching Hierarchy.
Voice signal (300 – 3100 Hz) – low pass filter (cutoff frequency 3.1 kHz) – Nyquist sampling rate = 6.2 kHz – actual sampling rate is 8 kHz.
Each of the 24 voice channels uses binary code with 8-bit word.
Frames
  for 8 kHz, each frame occupies a period of 125 µs
  contains 24 X 8 =192 bit words; plus 1 bit for sync = 193 bits
  bit duration = 0.647 µs (125µs/193bits); transmission rate is 1.544 Mb/s

## Slide 37
Example summery (The T1 System - a PCM system)
A TDM system is given such that:
N=24 Voice channels (300-3100) Hz.
Repeaters every (2-4) Km interval.
LPF with fc=3.1KHz
fs=8KHz.
8 bit / sample
mu-law (mu=255)
1) Find the frame length.
2) Find the number of bits/frame.
3) Find the number of bits/second.
4) Find the duration of each bit.

## Slide 38
Solution:
1) fs = 8KHz 🡺 Ts=1/fs =1/8000 = 125 µs (Ts is the frame length)
2) 24 Samples + 1 bit for synch 🡺 24(8) + 1=193 bits/frame .
3) 193 bits 125 µs 193 bits * 1 sec = 1.544Mb/s
??? 1 s 125 µs
4) 193 bits 125 µs 125 µs * 1 bit = 0.647 µs
1 bit ??? 193 bit
1)Find the frame length.
2)Find the number of bits/frame.
3)Find the number of bits/second.
4)Find the duration of each bit.

## Slide 39
DS0: Digital Signaling Zero, where the incoming signal has a 64kp/s rate (PCM).
DS1: Digital Signal one, it combines 24 DS0 bit stream to get 1.544Mb/s >(24(64)).
DS2: Combines 4-DS1 bit streams to obtain a 6.312 Mb/s >(4(1.544)).
DS3: Combines 7-DS2 bit streams to obtain a 44.736Mb/s >(7(6.312)).
DS4: combines 6-DS3 bit streams to obtain a 274.176Mb/s >6(44.736)).
DS5: combines 2-DS4 bit streams to obtain a 560.160Mb/s > 2(274.176).
Due to bit stuffing, the bit rate of a digital signaling produced by any of these multiplexers is slightly higher than the prescribed multiple of the incoming bit rate (i.e., DS1 =1.544 which is greater than 24*64)
Digital TDM Hierarchy (The North America Standard) .

## Slide 40: North American TDM Hierarchy.

## Slide 41: E1 System
E1 is a European digital transmission format devised by the ITU-TS and given the name by the Conference of European Postal and Telecommunication Administration (CEPT).
It’s an equivalent of the North American T-carrier system format.
E2 through E5 are carriers in increasing multiples of the E1 format.
E1's data rate is 2.048 Mbps, over 32 channels at 64/kbps each,
the E1 standard exceeds the transfer rates of it's equivalent system, T1 (1.544 Mbps over 24 channels.)

## Slide 42: Multiplexing

## Slide 43: Types of Multiplexing
Time Division Multiplexing
Code Division Multiplexing
Frequency Division Multiplexing
---------------------------------------------------------
Space Division Multiplexing
Polarization Division Multiplexing
Orbital Angular Momentum Multiplexing

## Slide 44: Multiplexing
FDM
Useful bandwidth of medium exceeds required bandwidth of channel
Each signal is modulated to a different carrier frequency
Carrier frequencies are separated so signals do not overlap (guard bands)e.g. broadcast radio
Channel are allocated even if there is no data
FDM
TDM

## Slide 46: Liner Prediction filter

## Slide 47
Linear Prediction
Finite – duration Impulse Response (FIR) discrete – time filter .
Z
-1
Z
Z
Z
-1
-1
-1
W1
W2
W3
Wp-1
Wp
X[n-2]
X[n]
X[n-1]
X[n-3]
X[n-p+1]
X[n-p]
input
Block of Linear Prediction filter of order P
Prediction X[n]
^
X[n] = X[n-1]W1 + X[n-2]W2 + X[n-3]W3 + …………+ X[n-p]Wp
^

## Slide 48
2
2
^

## Slide 50
Define ,
σx : variance of a sample of the process X(t) at nTs
σx = E [x [n] ] ..
Rx(kTs) : auto correlation of the process X(t) for a lag of kTs = Rx [k]
=Rx(k)= E[x[n] x[n-k]]
So ,
J =σx …. (check the book)
2
2
ΣWj Rx [k – j] = Rx [k] = Rx [-k] , k = 1,2,3…….P
Optimal equations
j=1
P
Wiener – Hopf equations for linear prediction .

## Slide 51
In matrix form, Let W = [ W1 W2 ……Wp ] , optimum coefficients vector
Px1
T
o
rx = [Rx [1] Rx[2] ………..Rx[p] ] , autocorrelation vector
Px1
Rx =
Rx[0] Rx[1]…………. Rx[p-1]
Rx[1] Rx[0] ………….Rx[p-2]
Rx[2] Rx[1] ………….Rx[p-3]
Rx[p-1] Rx[p-2] ………Rx[0]
Wiener – Hopf eqs ,can be written as :
optimum solution.
Rx Wo = rx
Wo = R rx
-1

## Slide 53
Linear Adaptive prediction
Wo = Rx rx requires knowledge of the autocorrelation function Rx [k] ,
k= 0,1,2,…….., P
What if Rx [k] is not a available ???
Solution : Use the “ adaptive prediction “ + recursive methods .
Linear predictor
Wk [n]
Z
+
-1
^
^
+
-
Input X[n]
Prediction
X[n]
Error e[n]
Block diagram- linear Adaptive prediction process
Least Mean Square LMS
Mean Square Error MSE
LMS
-1
LMS
MSE
…
To minimize error

## Slide 54: Comparing Encoding Techniques to speech signal

## Slide 55
3.17 MPEG Audio Coding Standard
Speech (voice) and Audio are similar in that the quality of a coding scheme is based on the properties of human auditory perception.
Speech speech production model is available so we have an efficient coding scheme (ADPCM).
Audio No production model is available .
MPEG-1 : Motion Picture Expert Group 1 .
MPEG-1/audio coding standard is a lossy compression system [like ADPCM] .
BUT it can achieve transparent, perceptually, lossless compression of stereophonic audio signals at high sampling rate.
Mean Opinion Score (MOS) test is used by MPEG committee with 6-to-1 compression ratio is good (indistinguishable) .
(original and coded audio signals are indistinguishable).
This is due to the usage of the characteristics of the human auditory system

## Slide 56
Digital Multiplexers (when signal is digital)
TDM is used to multiplex a group of analog signals after sampling them in time at a common (same) sampling rate .
If we have digital signals (with different bit rates) and we need to combine them into a single data stream (at a considerably higher bit rate than any of the inputs ) then we use a bit-by-bit interleaving procedure [digital multiplexing].
Multiplexer
High-speed
Transmission
line
Demultiplexer
1
2
N
1
2
N
Fig-diagram of a digital multiplexing - demultiplexing
bit-by-bit interleaving procedure.

## Slide 57
Multiplexing is accomplished by bit-by-bit interleaving; selector switch – sequentially scanning incoming line; at the receiving side – separation into low speed components.
Types of multiplexers:
  relatively low data bit rate user streams are TD multiplexed over the public switched telephone network.
  data transmission service by telecommunication carriers; part of the national digital TDM hierarchy.
Notes: mmmmmmm

## Slide 58
TDM
PCM
PCM
PCM
PCM
TDM
m1(t)
m2(t)
mN(t)
m1(t)
m2(t)
mN(t)
Byte interleaved TDM .
Analog Multiplixing followed by PCM
Bit interleaved TDM
PCM followed by digital multiplexing
Categories Digital Multiplexing

## Slide 59: Problems:
1. Digital signals cannot be directly interleaved into a format that allows for their separation automatically. Common clock or perfect synchronizations is needed.
The multiplexed signal must include some form of framing so the individual streams can be identified at the source.
The multiplexer should be able to handle small variations in bit rates – bit stuffing.

## Slide 60: Bit stuffing
To make the outgoing rate of the multiplexer a little bit higher than the sum of the max expected input rates.
Each input is fed into an elastic store at the multiplexer (reading can be done at different rate).
Identify stuffed bits – example AT&T M12 Multiplexer.

## Slide 61: Example: signal format of the AT&T M12 Multiplexer
Designed to combine 4 DS1 into one DS2 bit stream
Each frame contains a total of 24 control bits, separated by sequences of 48 data bits
4 frames, transmitted one after the other
12 bits from each input bit-by-bit interleaved, 48 bits
Four types of control bits – F,M and C inserted by multiplexer – total of 24 control bits