## Slide 1
  Digital Communications
  Digital Modulation (intro)
  4

## Slide 2: What makes a Communication System GOOD
We can measure the “GOODNESS” of a communication system in many ways:
  How close is the estimate to the original signal m(t)
    Better estimate = higher quality transmission
    Signal to Noise Ratio (SNR) for analog m(t)
    Bit Error Rate (BER) for digital m(t)
  How much power is required to transmit s(t)?
    Lower power = longer battery life, less interference
  How much bandwidth B is required to transmit s(t)?
    Less B means more users can share the channel
    Exception: Spread Spectrum -- users use same B.
  How much information is transmitted?
    In analog systems information is related to B of m(t).
    In digital systems information is expressed in bits/sec.

## Slide 3: What is modulation
Modulation is the process of encoding information from a message source in a manner suitable for transmission
It involves translating a baseband message signal to a bandpass signal at frequencies that are very high compared to the baseband frequency.
Baseband signal is called modulating signal
Bandpass signal is called modulated signal

## Slide 4: Modulation Techniques
Modulation can be done by varying the
  Amplitude
  Phase, or
  Frequency
  of a high frequency carrier in accordance with the amplitude of the message signal.
Demodulation is the inverse operation: extracting the baseband message from the carrier so that it may be processed at the receiver.

## Slide 5: Analog/Digital Modulation
Analog Modulation
  The input is continues signal
  Used in first generation mobile radio systems such as AMPS in USA.
Digital Modulation
  The input is digital.
  Used in current and future mobile radio systems

## Slide 6: A/D and D/A Conversion
Digital data to be carried on an analog signal.
A carrier signal (frequency fc) performs the function of transporting the digital data in an analog waveform.
The analog carrier signal is manipulated to uniquely identify the digital data being carried.

## Slide 7
Tomasi
Digital Modulation
AM
FM are replaced by Digital Modulation. (i.e., ASK, FSK, PSK)
PM
Digital communication systems are;
  Easy for process.
  Easy for multiplexing.
  Noise immunity .
A/D D/A
Analog Or digital signal
Destination
Channel

## Slide 10
FSK & PSK signals have a constant envelope, so they are preferred to ASK signals for passband data transmission over nonlinear channels.
phase –recovery circuit: ensures that oscillator supplying the locally generated carrier wave in the receiver is synchronized (frequency and phase) to the oscillator at the transmitter.
coherent digital modulation: If the receiver has a phase-recovery circuit.
non coherent: If the receiver has no phase-recovery circuit.
Digital Radio vs. Analog Radio (ASK,…)
1) In digital radio the modulating signals are digital pulses but the carrier signal is an analog one. (i.e., digital pulses modulate analog carrier).
2) Different modulation techniques are used in digital radio (ASK, FSK,…).
digital radio uses analog carriers to represent digital data.

## Slide 12
In a non-coherent FSK scheme, when we change from one frequency to the other, we do not adhere (stick) to the current phase of the signal
In coherent FSK, the switch from one frequency signal to the other only occurs at the same phase in the signal.

## Slide 13
Figure. Digital data over analog carrier

## Slide 14
Figure. Types of digital modulation

## Slide 15: note
Bit rate, N, is the number of bits per second (bps).
Baud rate (Symbol rate) is the number of signal elements per second (bauds).
In the analog transmission of digital data, the signal or baud rate (S) is less than or equal to the bit rate (N).
S=N/r bauds
Where r is the number of data bits per signal element (i.e., # of bits / sample ?).
baud rate=bit rate/r

## Slide 16: example
An analog signal carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.
Solution
Note: signal element== symbol===sample
r= 4 bits/symbol, S= 1000 symbols/second, and N (bit rate) is unknown.
(Bit rate) N = r*S = 4 bits/symbol * 1000 symbols/second
= 4000 bps

## Slide 17: example
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud.
-How many data elements are carried by each signal element?
-How many signal elements do we need?
Solution
-Given: N=8000 bps (bit rate), S = 1000 (baud rate or symbol rate).
-But both r and L are unknown. (r is # of bits per baud and L is # of levels)
1) r =N/S, 8000/1000=8 bits/baud
2) L (signal elements), L=2^r=2^8=256

## Slide 18
Shannon Limit for Information Capacity
C=B log (1+S/N) bits/sec .
C represents the number of independent symbols that can be carried out through the system in a given time.
C=B log (1+SNR) =3.32 B log (1+ SNR).
2
2
10
Example : Consider a standard voice-band communication channel with SNR of 1000 (30 dB) and a bandwidth of 2.7 kHz . Find the channel capacity.
Solution :
C=B log (1+SNR)=(2. 7K) log (1+1000) C= 26.9 kbps
The 2.7kHz bandwidth will carry 26.9 kbps. (this can not be done with a binary system. Hence, M-ary is needed )
2
2

## Slide 19
2.7 kHz bandwidth gives 27 kbps capacity.
Hence, each transmitted system must contain more thane one bit of information.
To achieve the Shannon limit (C) then digital transmission systems that have more than two output conditions (symbols) must be used.
Shannon Limit for Information Capacity
Example : Consider a standard voice-band communication channel with SNR of 1000 (30 dB) and a bandwidth of 2.7 kHz . Find the channel capacity.
Solution :
C=B log (1+SNR)=(2. 7K) log (1+1000) C= 26.9 kbps
The 2.7kHz bandwidth will carry 26.9 kbps. (this can not be done with a binary system. Hence, M-ary is needed )

## Slide 20
M- ARY Encoding
Binary FSK & binary PSK are binary systems (only two possible output 0, 1).
- BFSK & BPSK are M-ary systems with M=2 .
- it is better to encode at a level higher than binary ( M>2 ).
N = log M N: #of bits needed per symbol
M: # of output possible conditions with N bits
2
Input
output
Modulation
If 2-bits were allowed to enter a modulator before the output were allowed to change ,
2 = log M & M = 2 =4
2-bits
2
2
1
2
3
4
4- different
Output conditions.
N=1 M=2 = 2
N=2 M=2 = 4
N=3 M=2 = 8
3
1
2

## Slide 24
Amplitude Shift Keying - ASK
For AM V(t) = A/2 [1+ m(t)] cos ( 2* pi * fc*t).
modulating signal carrier signal
Let m(t)=+1 (binary) on – off-keying . (A cos(2*pi*fc*t) OR zero
OOK modulation .
V(t) = Am(t) cos(2*pi*fc*t). If m(t) = 0 or 1 ook
Double side band
_
dsb
DSB
OOK
carrier

## Slide 25: Amplitude Shift Keying (ASK)
ASK: changing the amplitude of a carrier signal to reflect the amplitude levels in the digital signal.
For example: a digital “1” could not affect the carrier signal, whereas a digital “0” would, by making it zero.
The line encoding will determine the values of the analog waveform to reflect the digital data being carried.

## Slide 26: Figure. Implementation of binary ASK (on-off keying, - OOK)

## Slide 27: Bandwidth of ASK
The bandwidth B of ASK is proportional to the signal rate S.
B = (1+d)S
“d” is due to modulation and filtering, 0<d<1
Figure. Binary amplitude shift keying (symbol, element or baud rate)

## Slide 28: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using ASK with d = 1?
Solution
Note: r=1 for BASK
fc = 250kHz., as the middle of the bandwidth (200-300).
B=100kHz. (which is 300-200)
B=(1+d)S  B=(1+1)S B=2S symbols/sec,
then, S=50k
S=N/r  N=S*r=50*1,  N=50 kbps
(here) Bit rate = half Bandwidth

## Slide 29: Example/ full-duplex
We normally use full-duplex links (both directions).
We divide the bandwidth into two bands each with a carrier frequency, as shown in the figure below.
It shows the positions of the two carrier frequencies and the bandwidths.
The available bandwidth for each direction is now 50 kHz,
The data rate is 25kbps in each direction.
Figure. Bandwidth of full-duplex ASK

## Slide 30
The digital data stream changes the frequency of the carrier signal, fc.
For example,
  “1” is represented by f1=fc +f,
  “0” is represented by f2=fc-f.
Frequency Shift Keying

## Slide 31: Bandwidth of FSK
If the difference between the two frequencies (f1 and f2) is 2f, then the required BW B will be:
B = (1+d)xS +2f
Fig. BFSK

## Slide 32: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulate this data using FSK with d = 1?
Solution
fc=250kHz. The midpoint of the band (200 to 300).
B=300-200 =100 kHz
B=(1+d)S+2Δf=2S+2Δf=100, then;
We chose 2Δf to be 50 kHz;  2S=50, S=25kbaud.
S=N/r N=r*S=1*25=25 kbps
Depends on Bit Duration?

## Slide 33: Multi Level FSK
Similarly to ASK then, FSK can use multiple bits per signal element.
That means we need to provision for multiple frequencies, each one to represent a group of data bits.
The bandwidth for FSK can be higher
B = (1+d)xS + (L-1)/2f
= LxS
Figure. Bandwidth of MFSK used in Example 5.6

## Slide 34
More than two frequencies are used
More bandwidth efficient but more susceptible to error

## Slide 35: Example A
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.
Solution:
-L = 23 = 8 (# of levels). S=N/r bauds
-The baud rate is S =bit rate/#of bits per symbol)
-So, S= 3 Mbps/3 bits per symbol  S=1 Mbaud.
-This means that the carrier frequencies must be 1 MHz apart (2Δf = 1 MHz).
-The bandwidth is B=LxS= 8 × 1M = 8MHz.
-Fig. A shows the allocation of frequencies and bandwidth.

## Slide 36
Solution (summary)
L= 8. (# of levels 8 carriers).
S = 3 Mbps  1 Mbaud.
fc = 1 MHz apart (2Δf = 1 MHz around each sub carrier).
bandwidth (B=LxS)  B = 8 × 1M = 8MHz.
Fig.A shows the allocation of frequencies and bandwidth.
Fig.A Bandwidth of MFSK used in Example A
What is the BW of each symbol?
What is the total BW required?

## Slide 37
Frequency Shift Keying - FSK
v(t) = Vc cos [(wc +( Vm (t) w )/2)t ]
v(t): binary FSK waveform .
Vc: peak unmodulated carrier amplitude.
wc: radian carrier frequency .
Vm(t): binary digital modulating signal.
w : change in radian output frequency .
Binary input
Analog output
0
1
0
1
fs
fm
fs
fm
Other form to present FSK

## Slide 38
fs : space frequency .
fm :mark frequency .
Time
freq
fm
fs
Binary FSK
fm > fs

## Slide 39
Bandwidth Consideration of FSK
Binary input
Analog output
FSK modulator (VCO)
1
0
1
0
1
0
0
1
1
0
0
0
1
0
T1
2T1
fa=fb/2
f=fb/4
tb
Highest fundamental frequency
Occurs when alternative 1/0 .
fb is the input bit rate AND fa is the baud (output) rate

## Slide 40
fb : input bit rate (bps).
tb : time of one bit = 1/fb .
T1 : period of shortest cycle .
1/T1 : fundamental frequency of binary, square wave.
Fastest input rate when the input is a series of alternating 1s & 0s.(square wave) .
Highest modulating frequency = 0.5 input rate
(i.e., output frequency fa = fb/2).

## Slide 41
1
1
1
0
tb
2 f
1/2tb
fc
fs=fc- f
fm=fc+ f
Carrier freq
FSK
modulator
Peak frequency deviation D f
f =abs(fm – fs) /2 = 1/4tb (Hz. minimum )
fs = fc -Df = fc – 1/4tb
fm = fc + Df = fc+ 1/4tb
For FSK :
B.W=( fm+ 1/tb) – (fs – 1/tb) = fm – fs +2/tb = 2( f + 1/tb ).
B.W=2(Df+ 1/tb)
1/tb
fs – 1/tb
fc
1/tb
fs
fm
fm+1/tb
FSK frequency spectrum (pulse sinusoidal wave have freq. spectrum that is ((sin x)/x)
B = (1+d)xS +2f

## Slide 42
Example:
Determine the bandwidth & baud for an FSK signal with a mark frequency of 51 kHz, a space frequency of 49 kHz , and a bit of 2 kbps.
Solution :
B.W = fm – fs +2/tb = 2( f + 1/tb ). OR BW=fm-fs+2fb (Note: 1/tb =bit rate?)
1) B.W = fm – fs + 2/tb
tb= 1/fb = 1/2000 = 0.5 msec.
B.W= 51000 – 49000+2/(0.5*10^-3) = 6000Hz .
2) With BFSK (r=1),
baud = input bit rate =2000 bits/sec

## Slide 43
-
+
Data output
FSK
Input
BPF
BPF
Envelop detector
Envelop detector
-
+
FSK
input
Data output
BPF
BPF
carrier
carrier
Non coherent FSK demodulator
coherent FSK demodulator
FSK Receiver
fs
fm

## Slide 44
amp
VCO
Phase compensator
Dc-error voltage
Analog FSK in
d
Binary data output
PLL
fs
fm
+V
0V
-V
Fig. PLL-FSK demodulator (most common)

## Slide 45
Minimum Shift –Keying (MSK) -MFSK
Similar to FSK but
fm & fs = n (fb / 2) , (n is odd)
fs & fb = n fb /n , (n is odd)
Phase discontinuties
fs = n (fb /2)
Sudden change in frequency, phase ??
This may create problems error
Fig . Non continuous FSK waveform (not MSK )
MSK is a form of continues – phase Frequency Shift Keying (CPFSK)

## Slide 46
Logic 1
Logic 0
Smooth continuoes transition
fm
fs
fb = 1kbps
MSK
Fig . Continuous-phase MSK waveform .( error is less)
fm : mark frequency .
fm = 5 (fb /2) = 5*1000/ 2 =2500 Hz .
fs = 3 (fb / 2) = 3*1000 /2 = 1500Hz .
5&3 not necessary to equal .

## Slide 47
Phase Shift Keying (BPSK).
Analog input
Binary digital signal
PM
PSK
Limited number of output phases
Binary PSK (BPSK) two phases
also called phase reversal keying (PRK)
or, pi phase modulation ( ) ?
1
0
1
Time
Time
tb
Binary input
BPSK
Output
Degree 0 180 0 180
Radian 0 pi 0 pi
Sin wc t
-Sin wc t
Sin wc t
-Sin wc t

## Slide 48
BPSK Transmitter
OUT PUT IS THE PRODUCT X.Y
+1V
-1V
Balanced (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0
FIG. Simplified block diagram of a BPSK Tx (Modulator).

## Slide 49
BPSK Receiver
Coherent
Carrier
Recovery
BPSK input
Balanced
Modulator
LPF
Binary data out
Logic +1
Tx
+sin(wc t)
Logic 0
-sin(wc t)
FIG . BPSK R x
Tx
+sin(wc t)
AND -sin(wc t)
+ 0.5
Logic 1
sin(wc t)
+sin(wc t)
-
X
fc <<2wc
BPSK
MOD
BPSK
MOD
- 0.5
Logic 0
Demo
Demo
Rx
Rx

## Slide 50
At point X :
sin wc t . Sin wc t out put of balanced mod.
Out 1 = sin wc t =0.5 (1-cos2wc t ) = 0.5 1.
Out 0 = -sin wc t = -0.5 (1-cos 2wc t )= -0.5 0 .
Filtered by the LPF
Filtered by the LPF
2
2

## Slide 51: PSK- Bandwidth consideration
We vary the phase shift of the carrier signal to represent digital data.
The bandwidth requirement, B is:
B = (1+d)xS
PSK is much more robust than ASK (i.e., noise is AWGN)
Figure. Binary phase shift keying

## Slide 52: Figure. Implementation of BPSK

## Slide 53: Bandwidth Consideration of BPSK (another way)
out put = sin(wa t) sin(wc t)
= 0.5 cos(wc – wa)t – 0.5 cos(wc+wa)t .
Widest output BW occurs when the input binary data are alternating.
The fundamental frequency (fa) of an alternating 1/0 bit sequence is fa=fb/2
Fundamental
Frequency of binary modulating signal
Un -modulated carrier
+1V
-1V
Balance (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0

## Slide 54
The minimum double-side Nyquist bandwidth (f N ) is
+1V
-1V
Balance (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0
Band width =input bit rate
=(1+d)S where d=0

## Slide 55
1
0
1
Time
Time
tb
Binary input
BPSK
Output
Degree 0 180 0 180
Radian 0 pi 0 pi
Sin wc t
-Sin wc t
Sin wc t
-Sin wc t
FIG. output phase vs. time for BPSK modulation
Figure Binary phase shift keying

## Slide 56
Example:
For a BPSK modulator with a carrier frequency of 70 MHz & an input bit rate of 10 Mbps. Determine the maximum & minimum upper & lower side frequencies , draw the output spectrum. Determine the minimum Nyquist bandwidth and calculate the baud.
Solution :
Out put spectrum
fc is suppressed .
B.W=10MHz
65 fc=70 75