## Slide 1: Quantization Techniques

## Slide 2: 1-Uniform Quantization
Quantization is the process of mapping a continuous range of amplitudes of a signal into a finite set of discrete amplitudes.
Quantizers can be thought of as devices that remove the irrelevancies in the signal and uses n bit can have M=2^n levels.
The SQNR of a PCM encoder (Check this formula)

## Slide 3: 2-Non Uniform Quantization:
Nonuniform quantizers with the feature that the step-size increase as the separation from the origin of the input-output amplitude characteristic is increased
m0 = -A
m1
m2 ……
0
mL=A

## Slide 4: Non Uniform Quantization:
Compression law:
  In US -law
  In Europe A-law

## Slide 5: Non Uniform Quantization:
Compander
Compressor Expandor
Compressor + Expandor = Compandor
F(x)
x[n]
Uniform Quantization
F1(x)
x[n]
Uniform Decoder
^

## Slide 6: 3-Adaptive Quantization:
Adaptive quantization with forward estimation (AQF).
Adaptive quantization with backward estimation (AQB)

## Slide 7: 4-Vector Quantization:
The vector quantizer that use blocks of consecutive samples of the source output to form vectors
The vector is encoded by comparing it with codebook consisting of a set of stored reference vectors known as code vectors or patterns
the coded transmission rate in bits per sample is given in terms of these parameters??

## Slide 8: ADPCM
PCM: speech to be encoded at a bit rate of 64 kbps
ADPCM: speech to be encoded at a bit rate of 32 kbps
  G.721, CT2 and DECT

## Slide 9: ADPCM

## Slide 10: Frequancy Domain Coding:
Sub Band Coding:
divide the entire speech band into unequal sub bands that contribute equally to the articulation index
Sub band Number Frequency range
1 200-700 Hz
2 700-1310 Hz
3 1310-2020 Hz
4 2020-3200 Hz
Sub band coding can be used for coding speech at bit rates in the range 9.6 kbps to 32 kbps

## Slide 11: Adaptive Transform Coding:
encode speech at bit rates in range 9.6 kbps to 20 kbps.
which involves block transformations of windowed input segments of the speech waveform

## Slide 12: Coding Methods - Examples
ZIP: no transformation nor quantization, apply VLC (LZW) to the stream of symbols in a file directly, lossless coding
PCM for speech: no transformation, quantize the speech samples directly using mu-law quantizer, apply fixed length binary coding
ADPCM for speech: apply prediction to original samples, the predictor is adapted from one speech frame to the next, quantize the prediction error, error symbols coded using fixed length binary coding
JPEG for image: apply discrete cosine transform to blocks of image pixels, quantize the transformed coefficients, code the quantized coefficients using variable length coding (runlength +Huffman coding)

## Slide 13: Example-Block diagram of a mobile radio transceiver

## Slide 14: Comparison of quality and transmission rate for various speech coding systems using MOS rating

## Slide 15
Relative complexity | MOS Quality | Bit rate (kbit/s) | Technique | Class
1 10 0.3 | 4.3 4.1 3 | 64 32 16 | PCM G.721 ADPCM G.721 DM | Waveform coders
30 | 4.3 | 64-48 | SBC(2) G.722 (7kHz) | Intermediate coder
50-100 | 3.2 | 4.8 | CELP/MPE for ½ rate GSM | Enhanced source coder
40 | 2 | 2.4 | LPC-10 vocoder | Source coder
Rate, performance and complexity comparison for various speech coder designs

## Slide 16: Mobile Source Coding-Introduction