## Slide 1: Fossil Fuel
Coal:
Coal is a fossil fuel created from the remains of plants that lived and died about 100 to 400 million years ago when parts of the earth were covered with huge swampy forests.
Coal is classified as a nonrenewable energy source because it takes millions of years to form.

## Slide 2: Coal
The energy we get from coal today comes from the energy that plants absorbed from the sun millions of years ago.
All living plants store solar energy through a process known as photosynthesis. When plants die, this energy is usually released as the plants decay.
Under conditions favorable to coal formation, however, the decay process is interrupted, preventing the release of the stored solar energy. The energy is locked into the coal.

## Slide 3: Coal
Millions of years ago, dead plant matter fell into swampy water and over the years, a thick layer of dead plants lay decaying at the bottom of the swamps.
Over time, the surface and climate of the Earth changed, and more water and dirt washed in, halting the decay process.
The weight of the top layers of water and dirt packed down the lower layers of plant matter.

## Slide 4: Coal
Under heat and pressure, this plant matter underwent chemical and physical changes, pushing out oxygen and leaving rich hydrocarbon deposits. What once had been plants gradually turned into coal.
Seams of coal—ranging in thickness from a fraction of an inch to hundreds of feet—may represent hundreds or thousands of years of plant growth.
One acre of this seam contains about 14,000 tons of coal.

## Slide 5: How Coal was Formed ?

## Slide 6: History of Coal
Native Americans used coal long before the first settlers arrived in the New World.
Hopi Indians, who lived in what is now Arizona, used coal to bake the pottery they made from clay.
European settlers discovered coal in North America during the first half of the 1600s.
They used very little at first. Instead, they relied on water wheels and wood to power colonial industries.

## Slide 7: History of Coal
Coal became a powerhouse by the 1800s.
People used coal to manufacture goods and to power steamships and railroad engines. By the American Civil War, people also used coal to make iron and steel. And by the end of the 1800s, people even used coal to make electricity.
When America entered the 1900s, coal was the energy mainstay for the nation’s businesses and industries. Coal stayed America’s number one energy source until the demand for petroleum products pushed petroleum to the front.

## Slide 8: History of Coal
Automobiles needed gasoline. Trains switched from coal power to diesel fuel.
Even homes that used to be heated by coal turned to oil or gas furnaces instead.
Coal production reached its low point in 1961. Since then, coal production has increased by more than 255 %, reaching a high record in 2008.
Today, coal supplies 21 % of the nation’s total energy needs, mostly for electricity production.

## Slide 9: Coal Mining
There are 2 ways to remove coal from the ground: Surface & Underground Mining.
Surface mining is used when a coal seam is relatively close to the surface, usually within 200 feet.
The first step in surface mining is to remove and store the soil and rock covering the coal, called the overburden.
Workers use a variety of equipment: draglines, power shovels, bulldozers & front-end loaders to expose the coal seam for mining.

## Slide 10: Coal Mining
After surface mining, workers replace the overburden, grade it, cover it with topsoil, fertilize and seed the area.
This land reclamation is required by law and helps restore the biological balance of the area and prevent erosion.
The land can then be used for croplands, wildlife habitats, recreation, or as sites for commercial development.

## Slide 11: Coal Mining
Although only about a third of the nation’s coal can be extracted by surface mining, more than two-thirds of all coal in the U.S. is mined using this method today. Why?
Surface mining is typically much less expensive than underground mining.
With new technologies, surface mining productivity has increased two and a half times since 1973.

## Slide 12: Underground (or Deep) Mining
Underground (or deep) mining is used when the coal seam is buried several hundred feet below the surface. In underground mining, workers and machinery go down a vertical shaft or a slanted tunnel called a slope to remove the coal. Mine shafts may sink as deep as 1,000 feet.
One method of underground mining is called room-and-pillar mining. With this method, much of the coal must be left behind to support the mine’s roofs and walls. Sometimes as much as half the coal is left behind in large column formations to keep the mine from collapsing.

## Slide 13: Underground (or deep) mining
A more efficient and safer underground mining method, called long wall mining, uses a specially shielded machine that allows a mined-out area to collapse in a controlled manner.
This method is called long wall mining because huge blocks of coal up to several hundred feet wide can be removed.

## Slide 14: Surface Mining and Deep mining

## Slide 15: Types of Coal
Coal is classified into four main types, depending on the amount of carbon, oxygen, and hydrogen present.
The higher the carbon content, the more energy the coal contains.
Lignite is the lowest rank of coal, with a heating value of 4,000 to 8,300 British thermal units (Btu) per pound.
Lignite is crumbly & has high moisture content.
Most lignite mined in the USA comes from Texas.
Lignite is mainly used to produce electricity.
It contains 25 to 35 % carbon.
About 7% of the coal mined in 2009 was lignite.

## Slide 16: Types of Coal
Subbituminous coal typically contains less heating value than bituminous coal (8,300 to 13,000 Btu per pound) and more moisture.
It contains 35 to 45 % carbon.
47% of the coal mined in 2009 in the U.S. was subbituminous.
Bituminous coal was formed by added heat and pressure on lignite. Made of many tiny layers, bituminous coal looks smooth and sometimes shiny. It is the most abundant type of coal found in the USA and has 2 to 3 times the heating value of lignite.

## Slide 17: Types of Coal
Bituminous coal contains 11,000 to 15,500 Btu per pound.
Bituminous coal is used to generate electricity and is an important fuel for the steel and iron industries.
It contains 45 to 86 % carbon.
46% of the coal mined in 2009 was bituminous coal.

## Slide 18: Types of Coal
Anthracite was created where additional pressure combined with very high temperature inside the Earth.
It is deep black and looks almost metallic due to its glossy surface.
It is found primarily in 11 northeastern counties of Pennsylvania.
Like bituminous coal, anthracite coal is a big energy producer, containing nearly 15,000 Btu per pound.
It contains 86 to 97 % carbon. Less than 1% of coal mined in 2009 was anthracite.