## Slide 1: Coal Reserves
When scientists estimate how much coal, petroleum, natural gas, or other energy sources there are in the World, they use the term reserves.
Reserves are deposits that can be harvested using today’s methods & technology.
Coal is found throughout the world. It is the most abundant fossil energy resource in the U.S. and the world, comprising 95% of U.S. fossil energy resources and 70% of world fossil energy resources on an energy content basis.
All coal ranks can be found in the U.S.

## Slide 2: Coal
Experts estimate that the US has about 262 billion tons of recoverable coal reserves.
If we continue to use coal at the same rate as we do today, we will have enough coal to last 146 to 234 years, depending on consumption rates.
This vast amount of coal makes the US the world leader in known coal reserves.

## Slide 3: Coal and the Environment
As the effects of pollution became more noticeable, the world decided it was time to balance the needs of industry and the environment.
Over a century ago, concern for the environment was not at the forefront of public attention.
For years, smokestacks from electrical and industrial plants emitted pollutants into the air.
Coal mining left some land areas barren and destroyed.
Automobiles, coming on strong after World War II, contributed noxious gases to the air.

## Slide 4: Coal and the Environment
The Clean Air Act & the Clean Water Act require industries to reduce pollutants released into the air & the water.
Laws also require companies to reclaim the land damaged by surface mining. Progress has been made toward cleaning and preserving the environment.
The coal industry’s largest environmental challenge today is removing organic sulfur, a substance that is chemically bound to coal.
All fossil fuels, such as coal, petroleum, & natural gas, contain sulfur.
Low sulfur coal produces fewer pollutants.

## Slide 5: Coal and the Environment
When these fuels are burned, the organic sulfur is released & combines with oxygen to form sulfur dioxide.
Sulfur dioxide is an invisible gas that has been shown to have adverse effects on air quality.

## Slide 6: Coal and the Environment
The coal industry is working to solve this problem.
One method uses devices called scrubbers to remove the sulfur in coal smoke.
Scrubbers are installed at coal-fired electric & industrial plants where a water and limestone mixture reacts with sulfur dioxide to form sludge.
Scrubbers eliminate up to 98 % of the sulfur dioxide.
Utilities that burn coal spend millions of dollars to install these scrubbers.

## Slide 7: Coal and the Environment
The coal industry has made significant improvements in reducing sulfur emissions.
Since 1989, coal-fired plants in the US have lowered sulfur dioxide emissions per ton by a fourth and have increased efficiency significantly.
Coal plants also recycle millions of tons of fly ash (a coal by-product) into useful products such as road building materials, cement additives..

## Slide 8: Coal and the Environment
CO2 is released when coal is burned, just as it is released from the human body during respiration.
CO2 combines with other gases, such as those emitted from automobiles, to form a shield that allows the sun’s light through the atmosphere, but doesn’t let the heat that is produced out of the atmosphere.
This phenomenon is called the Greenhouse Effect. Without this greenhouse effect, the Earth would be too cold to support life.

## Slide 9: Coal and the Environment
There is concern that human activities are causing major changes in greenhouse gas levels in the Earth’s atmosphere that are responsible for a change in the Earth’s climate.
Many scientists believe the Earth is already experiencing a warming trend due to the greenhouse effect.
Long-term studies by scientists in many countries are being conducted to determine the effect of changing greenhouse gas levels in the atmosphere.
Scientists are also researching new technologies to help mitigate changes to the global climate.

## Slide 10: Cleaner Coal Technology
Coal is the US’ most plentiful fossil fuel, but traditional methods of burning coal produce emissions that can reduce air & water quality.
Using coal can help the US achieve domestic energy security if we can develop methods to use coal that won’t damage the environment.
The Clean Coal Technology Program is a government & industry funded program that was begun in 1986 in an effort to resolve U.S. & Canadian concern over acid rain.

## Slide 11: Cleaner Coal Technology
Clean coal technologies remove sulfur & nitrogen oxides before, during, and after coal is burned, or convert coal to a gas or liquid fuel.
Clean coal technologies are also more efficient, using less coal to produce the same amount of electricity.

## Slide 12: Cleaner Coal Technology
Fluidized Bed Combustor:
One technique that cleans coal as it burns is a fluidized bed combustor.
In this combustor, crushed coal is mixed with limestone and suspended on jets of air inside a boiler.
The coal mixture floats in the boiler much like a boiling liquid.
The limestone acts like a sponge by capturing 90 % of the organic sulfur that is released when the coal is burned.
The bubbling motion of the coal also enhances the burning process.

## Slide 13: Cleaner Coal Technology
Combustion temperatures can be held to 1,500 degrees Fahrenheit, about half that of a conventional boiler.
Since this temperature is below the threshold where nitrogen pollutants form, a fluidized bed combustor keeps both sulfur and nitrogen oxides in check.

## Slide 14: Coal Gasification
Coal Gasification:
Another clean coal technology bypasses the conventional coal burning process altogether by converting coal into a gas.
This method removes sulfur, nitrogen compounds, and particulates before the fuel is burned, making it as clean as natural gas.

## Slide 15: Carbon Capture and Storage
Carbon Capture and Storage:
Research and demonstration projects are underway around the U.S. and world to capture carbon dioxide from power plants and store it deep underground in geologic formations.
Researchers are investigating the best ways to capture CO2, either before or after coal is combusted.

## Slide 16: Carbon Capture and Storage
The CO2 will then be compressed converting the gas to a liquid.
It will then be transported via pipeline to appropriate storage sites.
Three different types of locations have been identified as being able to hold CO2 :
Deep saline formations,
Oil and gas reservoirs that are near depletion or have been depleted &
Unmineable coal seams.