## Slide 1: Energy Science and Technology: Solar Energy
2018/2019

## Slide 2: Objectives
Understand the uses of Solar Energy in
  Heating and cooling
  Generating electricity
Understand the different mechanisms of concentrating solar energy

## Slide 3: Introduction
http://www.youtube.com/watch?v=NDZzAIcCQLQ
http://www.youtube.com/watch?v=4uPVZUTLAvA
Almost all of our energy is from solar energy
(through nuclear)

## Slide 4: Solar Energy
Uses of solar energy
Heating and cooling
(Chapter 2)
Generate electricity
Directly
(Photovoltaics)
(Chapter 3)
Indirectly
(Concentrating)
(Chapter 2)
Chapter 2: Solar thermal energy
Chapter 3: Solar Photovoltaics

## Slide 5: Solar Thermal Energy
Solar Thermal Systems
Passive
Active
Does not include mechanical equipment
Includes mechanical equipment (pumps, fans, etc)
Daylighting
Solar Thermal Engines
Active systems with concentrators
Making best use of natural light

## Slide 6
The nature and availability of solar radiation

## Slide 7: Characteristics
Introduction to Renewable Energy, by Vaughn Nelson, CRC Press Taylor & Francis Group, Boca, Raton, London, New York, 2011

## Slide 8: The Main Reactions
http://m.teachastronomy.com/astropedia/article/Nuclear-Reactions-in-the-Sun

## Slide 9: Introduction: Solar Energy
The sun is the central body of our planetary system; and is the star closest to the earth
Renewable Energy, by Martin Kaltschmitt . Wolfgang Streicher, and Andreas Wiese, Springer- USA 2007

## Slide 10: Parameters
Nucleus has temperatures of approximately 15x109 K.
Energy is released by nuclear fusion where hydrogen is melted to helium. The resulting mass loss (approximately 5x109 Kg/s) is converted into energy E.
Einstein: Energy is calculated by multiplying mass m and the square of the speed of light c:
E=mc2
Energy is released in the form of electromagnetic radiation

## Slide 11: Electromagnetic Radiation
Electromagnetic radiation mainly released by the photosphere covers the entire frequency from short-wave to long-wave radiation
Introduction to Renewable Energy, by Vaughn Nelson, CRC Press Taylor & Francis Group, Boca, Raton, London, New York, 2011

## Slide 12: Radiation from the Photosphere

## Slide 13: Radiant Flux Density
The radiant flux density of the sun, MS, is approximately 63.5x106 W/m2
The radiant flux density of the sun decreases with the square of the distance travelled
Radiant flux density at the outer rim of the earth atmosphere ESC can be calculated according to:

## Slide 14: Radiant Flux Density calculation
Diameter of sun dS is assumed up to photosphere (approx.1.39x109 m)
Mean distance between sun and earth (LES) is approx. 1.5 1011 m
The mean radiant flux density is approx. 1,370 W/m2 calculated at the top rim of the earth atmosphere. This mean value is called the solar constant.
Why does the radiant flux density change throughout the year?

## Slide 15: Position – On Earth
Longitude – from North to South, zero at Greenwich
Latitude – from East to West, zero at the equator
http://geographyworldonline.com/tutorial/latitudelongitude.jpg

## Slide 16: Position – Of the Sun
Altitude – between sun and horizon
Azimuth – between north and the projection of line from sun to Earth
Introduction to Renewable Energy, by Vaughn Nelson, CRC Press Taylor & Francis Group, Boca, Raton, London, New York, 2011

## Slide 17: Seasonal Variation
Caused by the elliptical orbit, where earth moves around the sun during the course of one year
What happens in the North Pole in summer and winter?

## Slide 18: Yearly intensities
Relative distance variation leads to fluctuation in radiation incident on the atmospheric rim
The solar constant reaches its maximum in January at almost 1,420 W/m2, due to reaching the shortest distance between the sun and the earth (Perihelion) on January.
The opposite takes place on July, when it reaches its minimum with approximately 1,330 W/m2 (Aphelion).
Renewable Energy, by Martin Kaltschmitt . Wolfgang Streicher, and Andreas Wiese, Springer- USA 2007

## Slide 19: Optimizing the Tilt
Tilt angle < latitude (in summer)
Tilt angle = latitude (in spring and autumn)
Tilt angle > latitude (in winter)
To maximize solar collection if you are on the northern hemisphere.

## Slide 20: Insolation
Solar radiation at the surface of the earth
Units: energy/sq. meter or power/sq. meter
Insolation
Direct
Perpendicular to the sun
Diffuse
Scattered from the atmosphere or reflected from objects on the surface

## Slide 21: Glazing
Before discussing solar heating and cooling, we must study glazing
Glazing
  Transparent material used for windows
  Covering that transmits solar energy
  Material can be glass (clear/coated/tinted) or plastics.

## Slide 22: Incident light
As light is incident on a material, it is either:
  Absorbed (α), or
  Transmitted (), or
  Reflected (ρ)

## Slide 23: Windows
Incident light is either transmitted, reflected, or absorbed
  Absorbed light is eventually reradiated
Transmittance depends of glazing material and angle of incidence
  Windows can be single or multiple layer

## Slide 24: The Magic of Glass
Transparent to visible light and short-wave infrared radiation
Opaque to long-wave infrared radiation

## Slide 25: Properties of Glazing Materials

## Slide 26: Heat Loss Mechanisms

## Slide 27: Windows U-value
Heat flow rate per square meter = U-value x temperature difference
How is this related to the equations we took before on heat transfer?

## Slide 28: Solar Heating
The amount of solar energy (insolation) that comes into a building depends on:
Window
  Size
  Orientation (normal, vertical horizontal)
  Glazing material
  Shading
Time of year
Location
Percentage sunshine (clouds, haze, clear)