## Slide 1: What is the fuel cell
Fuel cell is an electrochemical device converts the chemical energy taken from fuel to electrical energy.

## Slide 2: What is the fuel cell
Fuel cell
Fuel Like H2
Oxidant
Like O2
Electricity
Heat
Water
Secondary
Primary

## Slide 3: What is the fuel cell
It has a lot of application starting from portable devices to huge power plant.
50 Watt
1-200 MW

## Slide 4: What is the fuel cell
Facts
In 2010, fuel cell industry revenues exceeded a $750 million.
There were 140,000 fuel cell stacks shipped globally in 2010.
Annual growth rate of 115%.
Dominant producers of Fuel Cell is United States, Germany, Japan and South Korea.

## Slide 5: What is the fuel cell
The first fuel cell was proved in 1939 by William Grove.

## Slide 6: What is the fuel cell
The first use of fuel cell was in NASA space programs helped by General Electric.
In 1959, Thomas Bacon built 1 KW fuel cell.
United Technologies Corporation's power was the first company produced large power fuel cell systems gives 400 KW.

## Slide 7: How does the fuel cell work?
The fuel cell consist of four main parts :-
1- Anode (negative electrode):- it is the fuel supply part.
2- Cathode (positive electrode):- it is the oxidant supply part.

## Slide 8: How does the fuel cell work?
3- Catalysts: Is a chemical substance increases the reaction rate(platinum for the anode and nickel for the cathode)

## Slide 9: How does the fuel cell work?
4- Electrolyte :- Substance that allows positive ions to transfer within it. Because the membrane is electrically insulating.

## Slide 10: How does the fuel cell work?
A typical fuel cell produces a voltage from 0.6 V to 0.7 V at full rated load.
To deliver the desired amount of energy, the fuel cells can be combined in series and parallel circuits , where series yields higher voltage, and parallel allows a higher current to be supplied.

## Slide 11: Types of cells and fuels
Fuel cell Vs Battery
Battery:
1-Energy storage Device.
2-Amount of energy Determined by amount of Reactants .
3-In rechargeable batteries , the energy comes from external sources.

## Slide 12: Types of cells and fuels
Fuel cell Vs Battery
The Fuel cell is an energy conversion device NOT STORAGE DEVICE, it can produce Energy as much as you supply Fuel & oxidant .

## Slide 13: Types of cells and fuels
Hydrogen and oxygen is the most type of fuel and oxidant combination used .

## Slide 14: Types of cells and fuels
Why H2
1- High Reactivity when suitable catalysts Used .
2-The ability to produce it from Hydro carbons .
3-High Energy Density.

## Slide 15: Types of cells and fuels
Why O2
1-Readily exists from Air, means economically benefit .
2-Easly to store in close environment .

## Slide 16: Types of cells and fuels
Types of classification :-
1-Depending on type of fuel and oxidant.
2- Type of electrolyte.
3-Operation Temperature.
The Most Common Classification of fuel cells is by the type of electrolyte used in the cell .

## Slide 17: Types of cells and fuels
Main Types Of Fuel Cells
1-(PAFC): Polymer Electrolyte Fuel Cell.
2-(AFC): Alkaline Fuel Cell.
3-(PAFC): Phosphoric Acid Fuel Cell .
4-(MCFC): Molten Carbonate Fuel Cell.
5-(ITSOFC):Intermediate Temp. Solid Oxide Fuel cell.
6-(TSOFC):Tubular Solid Oxide Fuel Cell.

## Slide 18: Types of cells and fuels

## Slide 19: Applications

## Slide 20: Applications
There are many uses for fuel cells — right now, all of the major automakers are working to commercialize a fuel cell car. Fuel cells are powering buses, boats, trains, planes, scooters, forklifts, even bicycles.
Miniature fuel cells for cellular phones, laptop computers and portable electronics are on their way to market. Hospitals, credit card centers, police stations, and banks are all using fuel cells to provide power to their facilities.

## Slide 21: Applications
Wastewater treatment plants using fuel cells to convert the methane gas they produce into electricity.
Telecommunications companies are installing fuel cells at cell phone, radio and 911 towers. The possibilities are endless.

## Slide 22: Applications
Micro Power
Consumer Electronics- Fuel cells will change the telecommuting world, powering cellular phones, laptops and cell phone hours longer than batteries.
Companies have already demonstrated fuel cells that can power cell phones for 30 days without recharging and laptops for 20 hours.

## Slide 23: Applications

## Slide 24: Applications

## Slide 25: bicycle
The 20″ wheel prototype weighs 32kg and is powered by a PEM fuel cell and brushless electric motor. The top speed is 25km/hour and the 600L twin cylinder fuel cells have a maximum range of 100km.

## Slide 26: Advantages and disadvantages
Low emissions: fuel cells emit considerably less emissions than other combustion based technologies.

## Slide 27: Advantages and disadvantages
Very Low Noise and Vibrations : few moving parts means you will never hear a noise or feel the vibration.

## Slide 28: Advantages and disadvantages
Reliability & Maintenance considerably less moving parts and these require less maintenance.
Unlike batteries that must be disposed of once their chemicals are used up, fuel cell reactions do not degrade over time and can theoretically provide continuous electricity.

## Slide 29: Advantages and disadvantages
High efficiency : fuel cells are able to give efficiency more than other types of engines and other generators which can reach to (60-80)%.
Because fuel cells are clean and efficient at any size, they can be located almost anywhere.

## Slide 30: Advantages and disadvantages

## Slide 31: Advantages and disadvantages
Fuel Cells are currently very expensive, costing about 4500 dollars per kilowatt ,where diesel engine cost about 800-1000 dollars per kilowatt.
The danger of explosion of the compressed hydrogen due to increasing in temperature and pressure.

## Slide 32: Advantages and disadvantages
The shortage of materials used as a catalyst such platinum. But researchers works on this problem in two way:-
1- Find other material as catalyst.
2- Find other source of platinum and the used materials.
It produces significant amounts of carbon dioxide, which is a cause of global warming and greenhouse.