## Slide 1: 1.Tides
There are two high tides and two low tides around the Earth at any instant. One high tide is on the longitude closest to the Moon and the other on the longitude furthest from the Moon. The low tides are on the longitudes at 90◦ to the longitudes where the high tides are situated.
On any given longitude the interval between high tides is approximately 12 hours 25 minutes. The difference in height between a high tide and a low tide is called the
tidal range.

## Slide 2: 1.Tides
Tidal potential of some large tidal range sites

## Slide 3: Generating Power Methods
Tidal barrage.
Tidal stream generator.
Dynamic tidal power.

## Slide 4: Tidal barrage
The Rance Tidal Power Station, a tidal barrage in France. (1966)

## Slide 5: Tidal barrage
The barrage method of extracting tidal energy involves building a barrage across a bay or river that is subject to tidal flow. Turbines installed in the barrage wall generate power as water flows in and out of the estuary basin, bay, or river. These systems produces Static Head or pressure head (a height of water pressure). When the water level outside of the basin or lagoon changes relative to the water level inside, the turbines are able to produce power.

## Slide 6: Tidal barrage

## Slide 7: Tidal barrage
A rough estimate of the average power output from a tidal barrage can be obtained from a simple energy balance model by considering the average change of potential energy during the draining process. Consider a tidal basin of area A. The total mass of water in the tidal basin above the low water level is , where h is the tidal range. The height of the center of gravity is , so the work done in raising the water . Hence the average power output is
where T is the time interval between tides, i.e. the tidal period. In practice, the power varies
with time according to the difference in water levels across the barrage and the volume of water

## Slide 8: Tidal stream generator

## Slide 9: Tidal stream generator
Tidal stream generators draw energy from water currents in much the same way as wind turbines draw energy from air currents. However, the potential for power generation by an individual tidal turbine can be greater than that of similarly rated wind energy turbine. The higher density of water relative to air (water is about 800 times the density of air) means that a single generator can provide significant power at low tidal flow velocities compared with similar wind speed.

## Slide 10: Types of Tidal stream generator
Axial turbines
Vertical turbines
Vertical and horizontal axis crossflow turbines

## Slide 11: Wave Power
Wave power is the transport of energy by ocean surface waves, and the capture of that energy to do useful work — for example, electricity generation, water desalination, or the pumping of water (into reservoirs). Machinery able to exploit wave power is generally known as a wave energy converter (WEC).

## Slide 12: Application of Wave Power
Oscillating Water Column (OWC):
This method of generating power from the tide works by using a column of water as a piston to pump air and drive a turbine to generate power. This type of device can be fixed to the seabed or installed on shore.

## Slide 13: Application of Wave Power
Hinged Contour Device (Pelamis):
This snake like power converter generates electricity with three hydraulic pumps activated by hinged pontoons that move with passing waves. The Pelamis is loosely anchored so that most of the wave motion is absorbed by the device and converted to electricity .

## Slide 14: Application of Wave Power
Buoyant moored device :
This type of device floats on the surface of the water or below it. It is moored to the seabed by either a taught or loose mooring system. The Duck is shown in the figure below. Ducks work by independently rotating about a long linkage; this maintains its stability by out spanning wave crests. The front edge of the duck matches the wave particle motion. In moderate seas, the more cylindrical back portion creates no stern waves but when the weather is bad these parts shed energy through wave making to the rear. The device requires a depth of at least 80 meters and uses a system of weights and floats to give almost constant tension in the mooring cables.