## Slide 1: Daylight
Average DF | Appearance | Energy implications
< 2% | room looks gloomy | Electric lighting needed most of the day
2% to 5% | Predominantly daylight appearance, but supplementary artificial lighting is needed | Good balance between lighting and thermal aspects
> 5% | Room appears strongly daylight | Daytime electric lighting rarely needed, but potential for thermal problems due to overheating in summer and heat losses in winter
The daylight factor (DF) describes the ratio of inside luminance over outside luminance , expressed in percent

## Slide 2
Condition | Illumination | 
 | (ftcd) | (lux)
Sunlight | 10,000 | 107,527
Full Daylight | 1,000 | 10,752.7
Overcast Day | 100 | 1,075.3
Very Dark Day | 10 | 107.53
Twilight | 1 | 10.75
Deep Twilight | .1 | 1.08
Full Moon | .01 | .108
Quarter Moon | .001 | .0108
Starlight | .0001 | .0011
Overcast Night | .00001 | .0001
Luminance, is the amount of light measured in a plane. Illumenance is measured in foot-candles or lux in the metric system

## Slide 3
The inside illuminance can be considered as the sum of three sources:
Direct illuminance if the sky is visible from the considered point
Illuminance due to the reflections on the outside environment
Illuminance due to the reflections on the inside surfaces

## Slide 4
The outdoor light level is approximately 10,000 lux on a clear day. The inside building, in the area closest to windows, the light level may be reduced to approximately 1,000 lux. In the middle area it is may be as low as 25 - 50 lux.
Activity | Illumination (lux, lumen/m2)
Warehouses, Homes, Theaters, Archives | 150
Easy Office Work, Classes | 250
Normal Office Work, PC Work, Study Library, Groceries, Show Rooms, Laboratories | 500
Supermarkets, Mechanical Workshops, Office Landscapes | 750
Normal Drawing Work, Detailed Mechanical Workshops, Operation Theatres | 1,000
Detailed Drawing Work, Very Detailed Mechanical Works | 1,500 - 2,000