## Slide 1: Sampling process
Sampling is the process of converting continuous time, continuous amplitude analog signal into discrete time continuous amplitude signal
Sampling can be achieved by taking samples values from the analog signal at an equally spaced time intervals as shown graphically in Fig.1

## Slide 2: Sampling process
Fig.1

## Slide 3: Sampling
sampling theorem
  A real-valued band-limited signal having no spectral components above a frequency of Hz is determined uniquely by its values at uniform intervals spaced no greater than seconds apart

## Slide 4: Sampling types
There are three sampling types available, these are
  Ideal sampling
  Natural sampling
  Flat top sampling

## Slide 5: Ideal sampling
In ideal sampling the analog signal is multiplied by a delta comb functions as shown in Fig. 2
Fig.2

## Slide 6: Ideal sampling
Ideal sampling is used to explain the main concept of sampling theoretically
In practical life Ideal sampling can not be achieved, because there is no practical circuit which generates exact delta comb function

## Slide 7: Mathematical representation of ideal sampling
The sampled signal can be expressed mathematically in time domain as
The frequency domain representation of the sampled signal is given by

## Slide 8: Sampling
From the previous frequency domain equation and Fig. 2 we can see that the spectral density of is a multiple replica of
This means that the spectral components of is repeated at , , and so on up to infinity
The replicas of the original spectral density are weighted by the amplitude of the Fourier series coefficients of the sampling waveform

## Slide 9: Recovering the message signal from the sampled signal
The original analog signal can be recovered from its sampled version by using a low pass filter (LPF)
An alternative way to recover from is to multiply by the delta comb function again then using a LPF as was been done for the synchronous detection of DSB_SC signals
The latter method for recovery is not used in practice

## Slide 10: Effects of changing the sampling rate
If decreases, then increases and all replicas of moves farther apart
On the other hand if increases, then decreases and all replicas of moves closer to each other
When the replicas of overlaps with each other
This overlap is known as aliasing

## Slide 11: Aliasing effect
If the sampling frequency is selected below the Nyquist frequency , then is said to be under sampled and aliasing occurs as shown in Fig. 3
Fig. 3

## Slide 12: Time limited signals and anti aliasing filtering
In real life applications there are some signals which are time limited such as rectangular or triangular pulses
Those signals will have an infinite spectral components when analyzed using Fourier analysis
Those signal will suffer from aliasing since the sampling frequency should be infinite in order to avoid aliasing

## Slide 13: Time limited signals and anti aliasing filtering
This means the sampling frequency would not be practical
In order to limit the bandwidth of the time limited signal, a LPF filter is used
This filter is know as anti alias filter

## Slide 14: Natural sampling
In natural sampling the information signal is multiplied by a periodic pulse train with a finite pulse width τ as shown below

## Slide 15: Natural sampling
As it can be seen from the figure shown in the previous slide, the natural sampling process produces a rectangular pulses whose amplitude and top curve depends on the amplitude and shape of the message signal

## Slide 16: Recovering from the naturally sampled signal
As we have did in the ideal sampling, the original information signal can be recovered from the naturally sample version by using a LPF

## Slide 17: Generation of Natural Sampling
The circuit used to generate natural sampling is shown Below

## Slide 18: Generation of Natural Sampling
The FET in the is the switch used as a sampling gate
When the FET is on, the analog voltage is shorted to ground; when off, the FET is essentially open, so that the analog signal sample appears at the output
Op-amp 1 is a noninverting amplifier that isolates the analog input channel from the switching function

## Slide 19: Generation of Natural Sampling
Op-amp 2 is a high input-impedance voltage follower capable of driving low-impedance loads (high “fanout”).
The resistor R is used to limit the output current of op-amp 1 when the FET is “on” and provides a voltage division with rd of the FET. (rd, the drain-to-source resistance, is low but not zero)

## Slide 20: Pulse amplitude modulation PAM (flat top) sampling
In flat top sampling (PAM) the amplitude of a train of constant width pulses is varied in proportion to the sample values of the modulating signal as shown below

## Slide 21: Pulse amplitude modulation PAM (flat top) sampling
In PAM, the pulse tops are flat
The generation of PAM signals can be viewed as shown below

## Slide 22: Pulse amplitude modulation PAM (flat top) sampling
From the figure shown in the previous slide we can see that PAM is generated first by ideally sampling the information signal , then the sample values of are convolved with rectangular pulse as shown in part of the previous figure

## Slide 23: Pulse amplitude modulation PAM (flat top) sampling
The mathematical equations that describes the PAM in both time and frequency domain are described below
The impulse sampler waveform is given by
The sampled version of the waveform is given by

## Slide 24: Pulse amplitude modulation PAM (flat top) sampling
Note that represents an ideally sampled version of
The PAM pulses are obtained from the convolution of both and as described by the following equation

## Slide 25: Pulse amplitude modulation PAM (flat top) sampling
Frequency domain representation of the PAM can be obtained from the Fourier transform of as shown below
The above equation shows that the spectral density of the PAM pulses is not the same as that obtained for the sampled information signal

## Slide 26: Pulse amplitude modulation PAM (flat top) sampling
The presence of in the equation presented in slide 22 represent a distortion in the output of the PAM modulated pulses
This distortion in PAM signal can be corrected in the receiver when we reconstruct from the flat-top samples by using a low pass filter followed by an equalizing filter as shown in the next slide

## Slide 27: Recovering of f(t) from the PAM samples
The LPF and the equalizing filter are known as the reconstruction filter
However the equalizing filter can be ignored if the rectangular pulse width τ is small compared with the sampling interval and the ratio

## Slide 28: Why PAM is so common in communication although it generates spectral distortion
The reasons for using flat top sampling in communications are
  The shape of the pulse is not important to convey the information
  The rectangular pulse is an in easy shape to generate

## Slide 29: Why PAM is so common in communication although it generates spectral distortion
  When signals are transmitted over long distances repeaters are used. If the pulse shape is used to convey the information then repeaters must amplify the signal and therefore increase the amount of noise in the system. However if the repeaters regenerate the signal rather than amplifying it then no extra noise components will be added, therefore the signal to noise ratio for PAM system is much better than the that of the natural sampling pulses

## Slide 30: Generation of flat top samples
Flat top sampling can be generated by a circuit know as sample and hold circuit shown below

## Slide 31: Generation of flat top samples
As seen in Figure, the instantaneous amplitude of the analog (voice) signal is held as a constant charge on a capacitor for the duration of the sampling period

## Slide 32: Pulse width and pulse position modulation

## Slide 33: Pulse width and pulse position modulation
In pulse width modulation (PWM), the width of each pulse is made directly proportional to the amplitude of the information signal
In pulse position modulation, constant-width pulses are used, and the position or time of occurrence of each pulse from some reference time is made directly proportional to the amplitude of the information signal
PWM and PPM are compared and contrasted to PAM in Figure.

## Slide 34: Generation of PWM

## Slide 35: Generation of PPM

## Slide 36: Sampling example
A waveform, is to be uniformly sampled for digital transmission
What is the maximum allowable time interval between sample values that will ensure perfect signal reproduction?
If we want to reproduce 1 minute of this waveform, how many sample values need to be stored?
Two analog signals and are to be transmitted over a common channel by means of time-division multiplexing. The highest frequency of is 3 kHz, and that of is 3.5 kHz. What is the minimum value of the permissible sampling rate?

## Slide 37: Sampling example
Solution
The maximum allowable time interval between samples can be found from the sampling theorem as
The number of samples per minute is equal to
The minimum value of the sampling rate will be