## Slide 1: Microwave link design
Microwave link is a wireless communication channel that transmits and receives information on microwave frequencies ( 2 to 80 GHz) as shown

## Slide 2: Why do we use microwave link
Microwave link is used in connecting terrestrial areas, and in areas where it is either difficult or costly to connect via cables
Microwave links are widely used in Satellite communications, WiFi, and in Cellular networks

## Slide 3: Advantages of Microwave link
Less affected by natural calamities
Less prone to accidental damage
Links across mountains and rivers are more economically feasible
Single point installation and maintenance
Single security point
Quickly deployed

## Slide 4: Topics to be covered in microwave link design
The following topics must be covered when a microwave link is designed
Antenna fundamentals (gain, directivity, radiation pattern and type)
Fresnel zone
Friss formula and Free space loss and other types of losses
Link budget and Fade margins
Effect of noise
Fading and fade margins calculation

## Slide 5: Line of sight (LOS) considerations
Microwave links requires a clear line of sight conditions
Radio LOS takes into account the concept of Fresnel ellipsoids and their clearance criteria
The Fresnel zone must be clear of all obstructions

## Slide 6: Fresnel zone definition
Fresnel zone are defined as areas of constructive and destructive interference
Fresnel zones are created when electromagnetic wave propagation in free space is reflected (multipath) or diffracted as the wave intersect obstacles.
Fresnel zones are specified employing integer numbers that correspond to the number of half wavelength multiples that represent the difference in radio wave propagation path from the direct path

## Slide 7: Graphical representation of Fresnel zone

## Slide 8: Fresnel zones formation
To understand how the Fresnel zone is formed consider an electromagnetic wave sent from point to point through the two paths shown below

## Slide 9: Fresnel zones formation
Two signal copies will be received at point R
The first signal copy follows a direct path , while the second signal copy is received through
The total signal received at point is the phasor sum of the direct signal and the reflected signal
The reflected signal will be received with a time delay due to the longer travelling path

## Slide 10: Fresnel zones formation
The time delay equivalent to a phase delay
Where is the difference in the traveling path and is the speed of light
can be determined from

## Slide 11: Fresnel zones formation
Therefore we can write
If , and , we can use the binomial series expansion to simplify the expression

## Slide 12: Fresnel zones formation
By using the above approximation can be further simplified by
Now the phase delay expression became as given by

## Slide 13: Fresnel-Kirchhoff diffraction parameter
The Fresnel-Kirchhoff diffraction parameter is defined by
Therefore we can rewrite
If the diffraction point is below the line of sight (LOS), then is negative and will also be negative

## Slide 14: Effect of the blockage object on and
When the diffraction point is located on the LOS, and are both equal to zero. If the blockage is the horizon, then the “ and equal zero” case corresponds to the maximum LOS

## Slide 15: Fresnel zones formation
Note that the received signal at point will be faded if the received signals at that point is out of phase
The phase shift occurs when or when ; where is an odd integer
This means that
Or we can find an expression for as a function of

## Slide 16: Fresnel zones formation
The equation for defines a sequence of ellipsoids with the transmit and receive antennas as the foci as shown below

## Slide 17: Fading zones
Note Fresnel zones whose path difference odd multiple of will be a zones of destructive interference
The zones with even will be zones with constructive interference (the signal will be stronger at these values of )

## Slide 18: Notes about the Fresnel zones
The Fresnel zone is three dimensional ellipsoids
Reflectors/diffractors within the field of view should not be near to an odd multiple Fresnel zone boundary to avoid signal loss (destructive interference)
For most microwave links (communication systems) if the Fresnel zone is clear of any obstruction in the first 60% of the first zone will be sufficient to consider good line of sight communication system
Any obstruction object located outside the , will not cause a loss of more than

## Slide 19: Fresenl zone and the clearance

## Slide 20: Fresnel zone example
Consider a point to point communication system, with and . If there is a building present, 300 m from one end of the link, how far must it be (in elevation or height) from the LOS to avoid signal fading (destructive interference regions)

## Slide 21: Solution
The obstruction object should be away , therefore
If the building is away from the one end of the link, then
So the rooftop must be at least 0.9 m below the LOS to keep the first Fresnel zone 60% clear

## Slide 22: Solution
It is also important that the rooftop not be near one of the odd Fresnel zone boundaries to prevent destructive interference from reflections

## Slide 23: Diffraction loss
Diffraction loss occurs when an obstacle is located near by the communication link
Diffraction can attenuate the received signal level and significantly affects the performance of the microwave link

## Slide 24: Diffraction loss calculations
Diffraction loss attenuation (diffraction integral) can be calculated based on the knife edge diffractor
The loss due to diffraction can be approximated by

## Slide 25: Diffraction loss versus
The diffraction loss for different values of the Fresnel-Kirchhoff diffraction parameter can be best illustrated by the following diagram

## Slide 26: Fresnel-Kirchhoff diffraction parameter
Recall that the Fresnel-Kirchhoff diffraction parameter is defined by is defined by

## Slide 27: Obstacle losses and knife-edge approximation

## Slide 28: Diffraction loss example
Consider a communication link comprised of two 150-MHz hand-held radios separated by 1 km as shown below. The barrier between the two radios runs perpendicular to the line of sight and is 5 m below the line of sight. Assume that the barrier is a thin, solid fence that is 200 m from one end of the link. How much additional path loss (beyond free-space loss) can be expected due to the diffraction from the fence?

## Slide 29: Solution
The Fresnel-Kirchhoff diffraction parameter can be found from

## Slide 30: Solution
Therefore we can write
From slide 19, we can find the diffraction integral is given by

## Slide 31: Loss/attenuation
There are different loss/attenuation mechanimsms that will attenuates the microwave signal when it propagates from the transmitter to the receiver. Some of the losses are
  propagation (path) loss
  Vegetation loss
  Gas absorption
  Rain attenuation
  Antenna misalignment
  Miscellaneous losses
Some of these loss mechanisms will be discussed in in the next few slides

## Slide 32: Free space loss (path loss)
Electromagnetic waves are attenuated when propagating between two points
The free space loss is used to predict the received signal strength when the receiver and the transmitter have a clear, unobstructed line of sight path
The attenuation is directly proportional to the square of the distance and frequency between the transmitter and the receiver

## Slide 33: Free space loss (path loss) is the dominant attenuation mechanism
Free space loss represents most of the total attenuation of the electromagnetic signal
The free space loss can be derived from Friis transmission equation
Friis showed that if there is a transmitting and receiving antennas separated by a distance , then the power received by the receiving antenna is given by

## Slide 34: Free space loss (path loss)
Where
and is the transmitted and received powers respectively,
and are the gains of the transmitter and receive antennas

## Slide 35: Free space loss (path loss)
From the above equation, it is clear that the free space loss is given by
Where

## Slide 36: Free space loss equation in dB
The above equation for the free space loss can be expressed in dB as shown below
If the distance between the transmitter and the receiver is expressed in miles, then the above equation can be modified as shown

## Slide 37: FSL doubling/halving the distance
Doubling the distance between the transmitter and the receiver increase the loss by
On the other hand if the distance between the transmitter and the receiver is halved then the FSL is reduced by as illustrated by the following table
Doubling the frequency will result in in crease in FSL

## Slide 38: Effective Isotropic Radiated Power (EIRP)
The Effective Isotropic Radiated Power (EIRP) is defined as the power radiated from an isotropic antenna
An isotropic antenna is an ideal antenna that radiates or receives equally in all directions
Mathematically the EIRP is defined by

## Slide 39: Fade margin (Link margin)
The fade margin (link margin) is defined as the difference between the received signal power level and the minimum signal power level (threshold) that achieves a certain average probability of bit error (or a certain signal to noise ratio), therefore we can write
Where is the fade margin in , is the receiver threshold in and is the received signal in

## Slide 40: Link budget
The link budget analysis of a wireless communication system is an equation that relates the received signal power with the transmitted signal power , antenna gains and the total loss/attenuation mechanisms of an electromagnetic wave
The link budget in dB can be obtained from Friis equation directly which can be expressed mathematically by

## Slide 41: Link budget and wireless link planning
The link budget is a useful tool in planning wireless link
The link budget can be used to determine the maximum distance between transmit and receive antennas at a particular frequency
The distance can be planned to achieve for a given signal to noise ratio\average probability of bit error requirements

## Slide 42: Fade margin (Link margin)
We can re-express the fade margin expression by using the Friis formula as given below
Now, the fade margin is given by,
Note that the , therefore

## Slide 43: Link budget example
Consider a communication link operates in free space at . Assume that the transmit power is , and both transmit and receive antennas have a gain of . If the distance between the transmitter and the receiver is and the receiver threshold is . Determine
The path loss (free space loss) in dB
The Effective Isotropic Radiated Power EIRP in dB and dBm
The fade margin (link margin)

## Slide 44: Solution
The free space loss is
The EIRP is defined by
If we want to convert the power from to we simply use the following equation

## Slide 45: Solution

## Slide 46: Dynamic range of the receiver
The dynamic range of communication receiver is mainly controlled by the low noise amplifier as shown by
The dynamic range in dB is defined mathematically by
The 1 dB compression point is the point where the output power is below its linear value by 1 dB

## Slide 47: popular receiver architectures
In the early communications system there were different receiver architectures
  The first was the tuned radio frequency receiver
  The second was the super-heterodyne receiver
  The third type is the direct conversion receiver
  Another type of receivers is digital down conversion receiver is designed by under sampling the RF signal
Only the super-heterodyne receiver will be considered

## Slide 48: The super heterodyne receiver
The super works by shifting the frequency of the RF input signal to the frequency of the receiver IF filter
Super heterodyne receiver

## Slide 49: The super heterodyne receiver
The main advantage of the super heterodyne receiver is that the same high quality IF filter can be used for all input signals
The frequency selection is made by varying the local oscillator frequency
The super heterodyne receiver suffers from the image frequency problem

## Slide 50: Image frequency
The image frequency occurs when two RF signals separated by are fed to the input of the receiver such that
The receiver will detect both signals at simultaneously
This results in an unwanted distortion at the receiver
The signal with the is called the image of the signal with one of the solutions to this problem is to select
The other solution is to use an image reject filter which is a tunable BPF at the input of the receiver

## Slide 51: Image frequency example
Consider a receiver with the IF filter centered at 455 kHz. If it is desired to receive a 1 MHz input signal, the local oscillator is tuned at 1.455 MHz. Determine the image frequency that correspond t the 1 MHz signal.
Solution
The image frequency is determined from the relation

## Slide 52: Effect of noise on the microwave link
The key receiver characteristic that determines wireless link (microwave in our case) is the receiver threshold or receiver sensitivity
The receiver threshold is the minimum detectable signal in noise that result in a given signal to noise ratio
Thermal noise, nonlinearities of the amplifiers, local oscillator phase noise, intermodulation distortion, and synchronization loss contribute in noise and degrades the receiver performance

## Slide 53: Thermal Noise
Receiver noise is caused by the thermal motion of electrons, called Browning motion, in the front end of the receiver
This noise is modelled as a random variable with Gaussian distribution and a power spectral density of
Thermal noise is additive in nature and does not depend on the received signal

## Slide 54: Thermal noise expression
The input thermal noise power generated within a matched receiver is defined by
Where
  is the input noise power
  is the Boltzman’s constant
  is the standard noise temperature in kelvin
  is the equivalent noise bandwidth, which can be approximated by

## Slide 55: Thermal noise
Note that the term which is defined as the single sided power spectral density of the AWGN
Normally the receiver circuit elements (resistors, amplifier, mixer, local oscillator) adds additional noise, therefore the noise power at the receiver output is given

## Slide 56: Thermal noise
Where
  is the noise added by the receiver
  is the receiver equivalent noise temperature
  is the noise figure of the receiver

## Slide 57: Noise figure F
The noise figure is a factor that can be used to describe how much noise added to the received signal by the receiver components
It is defined by
The noise factor can also be defined as

## Slide 58: Noise figure and noise temperature
The noise added by the receiver elements can be also described by the noise temperature
The noise temperature is related to the noise figure by
Where is the equivalent noise temperature of the receiver, is the room temperature in Kelvin
is the noise figure of the receiver

## Slide 59: Receiver output noise
The noise power at the receiver output can be computed by one of the following expressions
Where is the system equivalent noise temperature

## Slide 60: Effect of the thermal noise on the receiver performance
Thermal noise added by the receiver elements will degrade the signal to noise ratio at the receiver output
The added noise will increase error of the received data
However the design of wireless link may require increasing the received signal power at the input of the receiver to account for thermal noise
Increasing the received signal power can be made by changing one of the parameters of the link budget equation (such as reducing d, or increasing EIRP or minimizing attenuation or increasing the antenna size)

## Slide 61: Thermal noise example
Given a receiver for a 10-megasymbol-per-second signal, determine
Find the noise figure of the receiver if the equivalent noise temperature of the receiver is 870K
The noise bandwidth
The available noise power present with the signal
Determine also the average probability of error if QPSK modulation is used and the energy per bit is

## Slide 62: Solution
The noise figure of the receiver is given by
The noise bandwidth is given by
The output noise power of the receiver is
The average probability of bit error is given by

## Slide 63: Example
A given microwave receiver has a bandwidth of 50 MHz, a noise figure of 7 dB. Determine the receiver threshold (minimum detectable) if the required signal to noise ratio at the receiver output is 12 dB for reliable microwave link

## Slide 64: Solution
The signal to noise ratio is defined by

## Slide 65: Importance of noise in receiver system
Recall that most RF receivers are composed from the following Block diagram
Each block in the receiver adds a thermal noise to the received signal

## Slide 66: Importance of Noise in receiver system
The noise added to the signal picked by the antenna will degrade the SNR at the output of the receiver
This reduces the receiver sensitivity (threshold)
It also increase the total noise figure of the receiver

## Slide 67: Noise figure in cascaded system
What is the overall noise factor in cascade system where more than one blocks are cascaded together?
It can be proved that the noise factor of the cascaded system is given by
And the system effective noise temperature is given by

## Slide 68: Noise factor of cascaded networks
Example: for the system shown in the figure determine the overall system noise figure. If the input noise power from a feeding antenna is , where . Find the output noise power in . If we require a minimum signal to noise ratio (SNR) of 20 dB at the receiver output what is the minim signal voltage that should be applied

## Slide 69: Noise factor of cascaded networks
Solution: the overall noise figure of the cascaded system is given by
Now the overall noise figure is given by
The output noise power is defined by

## Slide 70: Noise factor of cascaded networks
Solution: The receiver threshold can be determined from
The magnitude of the voltage signal seen by the receiver can be determined from
The input impedance of the receiver is

## Slide 71: Relation between and the SNR
The designer of digital modulation modem uses to describe the error performance of the system
is defined the energy per symbol divided by the power spectral density of the noise power
However is related to the signal to noise ratio by the following relation

## Slide 72: Vegetation attenuation loss
Line of sight between stations is required for point to point microwave links
However trees and plants are continuously growing
The growing trees and plants might intercept the Fresnel zone and cause signal attenuation
When designing a microwave link it is important to include a provision for at least ten years of vegetation growth

## Slide 73: Gas Absorption

## Slide 74: Gas Absorption

## Slide 75: Fading
Fading is defined as the variation of the strength of the received radio carrier
Fading types are
  Multipath fading which is composed from flat fading and/or frequency selective fading
  Rain fading
  Refraction-diffraction fading (k-type fading)

## Slide 76: Rain fading
The rain fading is described by different models
The most widely used models are
  The first model which is the most widely used was developed by the International Telecommunications Union Radio Section (ITU-R)
  The second model is the Crane model (used mainly in the united states)

## Slide 77: Reducing the Effects of Rain
The effect of rain can be reduced by using two main design principles
Reduce the link frequency under 10 GHz. For links designed in the C-band (4-6 GHz) the rain attenuation rarely exceeds 1 or 2 dB
Use adaptive modulation. In adaptive modulation, the symbol rate is reduced when the rain attenuation increases. The concept of adaptive modulation is best illustrated in the next slide

## Slide 78: Adaptive modulation

## Slide 79: Interference Fade Margins
Interference in microwave systems is caused by the presence of an undesired signal in a receiver
Interference into a digital radio will degrade the receiver threshold and result in a lower effective fade margin, thus producing excessive bit errors or frame losses as the radio fades near threshold

## Slide 80: Interference Fade Margins
Adjacent-channel interference fade margin (AIFM) (in decibels) accounts for receiver threshold degradation due to interference from adjacent channel transmitters in one’s own system
Interference fade margin (IFM) is the depth of fade to the point at which RF interference degrades the BER to

## Slide 81: Example
What is the free space loss for a signal operating at and a range of

## Slide 82: Solution
The free space loss can be estimated by using the following equation

## Slide 83: Example
A transmitter has an output of at a carrier frequency of . Assume that the transmitting and receiving antennas are parabolic dishes each in diameter. Assume that the efficiency of each antenna is 0.55
Evaluate the gain of each antenna
Calculate the ERIP
If the receiving antenna is located 25 miles from the transmitting antenna over free-space path, find the received signal

## Slide 84: Solution
The antenna gain is defined as
The physical area of the antenna is

## Slide 85: Solution
The ERIP can be found from
The received signal power can be determined from

## Slide 86: Example
The direct broadcast system in North America operates at 12.2–12.7 GHz, with a transmit carrier power of 120 W, a transmit antenna gain of 34 dB, an IF bandwidth of 20 MHz, and a worst-case slant angle (30◦) distance from the geostationary satellite to Earth of 39,000 km. The 18-inch receiving dish antenna has a gain of 33.5 dB and sees an average background brightness temperature of , with a receiver low-noise block (LNB) having a noise figure of 0.7 dB. The required minimum CNR is 15 dB. The overall system is shown in the next slide

## Slide 87: Example
Find
The link budget for the received carrier power at the antenna terminals
The receiver figure of merit for the receive antenna and LNB system
The CNR at the output of the LNB
The Link margin of the system

## Slide 88: Solution
The link budget can be determined from

## Slide 89: Solution
The receiver figure of merit is
Now

## Slide 90: Solution
The carrier to noise ratio CNR at the output of the LNB is given by

## Slide 91: Solution
The link margin (Fade margin) is given by

## Slide 92: Example
A given satellite transmitter operates at has an ERIP of . Assume that the only loss affecting the system is the free space loss. Assume that satellite transmit digital data at a rate of . Assume that the required signal to noise ratio at the receiver output is . The system temperature at the receiver is , the receiving antenna efficiency is
What is the minimum dish diameter that can be used

## Slide 93: Solution
The required received signal power can be determined from as shown

## Slide 94: Solution
From the link budget equation we can estimate the gain of the receiving antenna as
The Gain of the receiving antenna is given by

## Slide 95: Example
Design a microwave link operating at 28 GHz, using 30-dB dish antennas at each end. A 10-dB fade margin is required to allow for rain fades. If the transmit power is 0 dBm, the receiver noise figure is 7dB, the bandwidth is 50 MHz, and the required carrier-to-noise ratio for reliable operation is 12dB. In your design find the following:

## Slide 96: Example
  The required received signal level
  The allowable path loss
  The maximum allowable range
  The minimum antenna heights if a tall building is located 1 km from the transmitting antenna

## Slide 97: Solution
The required received signal level can be determined from the fade margin
The receiver threshold can be determined from the carrier to noise ratio
Now the fade margin is 10 dB

## Slide 98: Solution
The path loss can be determined from the link budget equation
The maximum allowable range can be found from

## Slide 99: Solution
Antenna heights can be determined from Fresnel zone calculations
The minimum antenna height to keep the Fresnel zone clear is

## Slide 100: Detailed link budget