## Slide 1: Chapter 7: Food Preservation through Temperature Reduction 1. Freezing 2. Chilling
By:
Dr. Mohammed Sabbah
An-Najah National University
Faculty of Agriculture

## Slide 2
Freezing: is the unit operation in which the temperature of a food is reduced below its freezing point and a proportion of the water undergoes a change in state to form ice crystals.
The immobilisation of water to ice and the resulting concentration of dissolved solutes in unfrozen water lower the water activity (aw) of the food
Preservation is achieved by a combination of low temperatures, reduced water activity and, in some foods, pre-treatment by blanching.
1. Freezing

## Slide 3: The major groups of commercially frozen foods are as follows:
• fruits (strawberries, oranges, raspberries) either whole or pureed, or as juice concentrates
• vegetables (peas, green beans, sweet corn, spinach, and potatoes)
• fish fillets and sea foods (cod, plaice, shrimps and crab meat) including fish fingers, fish cakes or prepared dishes with an accompanying sauce
• meats (beef, lamb, poultry) as carcasses, boxed joints or cubes, and meat products (sausages, beefburgers, reformed steaks)
• baked goods (bread, cakes, fruit and meat pies)
• prepared foods (pizzas, desserts, ice cream, complete meals and cook–freeze dishes).

## Slide 4: 2. Theory
During freezing, sensible heat is first removed to lower the temperature of a food to the freezing point.
In fresh foods, heat produced by respiration is also removed. This is termed the heat load, and is important in determining the correct size of freezing equipment for a particular production rate.
A substantial amount of energy is therefore needed to remove latent heat, form ice crystals and hence to freeze foods.

## Slide 5: Time–temperature data during freezing.
If the temperature is monitored at the thermal centre of a food (the point that cools most slowly) as heat is removed, a characteristic curve is obtained.

## Slide 6
1- AS The food is cooled to below its freezing point 0f which, with the exception of pure water, is always below 0 ºC. At point S the water remains liquid, although the temperature is below the freezing point. This phenomenon is known as supercooling and may be as much as 10 ºC below the freezing point.
2- SB The temperature rises rapidly to the freezing point as ice crystals begin to form and latent heat of crystallisation is released.

## Slide 7
3- BC
Heat is removed from the food at the same rate as before, but it is latent heat being removed as ice forms and the temperature therefore remains almost constant.
It is during this stage that the major part of the ice is formed .
4- CD One of the solutes becomes supersaturated and crystallizes out. The latent heat of crystallization is released

## Slide 8
5- DE Crystallisation of water and solutes continues. The total time tf taken (the freezing plateau هضبة التجمد) is determined by the rate at which heat is removed.
6- EF
The temperature of the ice–water mixture falls to the temperature of the freezer.
A proportion of the water remains unfrozen at the temperatures used in commercial freezing; the amount depends on the type and composition of the food and the temperature of storage. For example at a storage temperature of -20 ºC the percentage of water frozen is 88% in lamb, 91% in fish and 93% in egg albumin.

## Slide 10
During freezing, heat is conducted from the interior of a food to the surface and is removed by the freezing medium.
The factors which influence the rate of heat transfer are:
• the thermal conductivity of the food
• the area of food available for heat transfer
• the distance that the heat must travel through the food (size of the pieces)
• the temperature difference between the food and the freezing medium
• the insulating effect of the boundary film of air surrounding the food.
• packaging, if present, is an additional barrier to heat flow.

## Slide 11: Equipment
The selection of freezing equipment should take the following factors into consideration:
the rate of freezing required;
the size, shape and packaging requirements of the food; batch or continuous operation,
the scale of production, range of products to be processed and not least the capital and operating costs.

## Slide 12
Freezers are broadly categorized into:
• mechanical refrigerators, which evaporate and compress a refrigerant in a continuous cycle and use cooled air, cooled liquid or cooled surfaces to remove heat from foods
• cryogenic freezers الثلاجات المبردة, which use solid or liquid carbon dioxide, liquid nitrogen (or until recently, liquid Freon) directly in contact with the food.

## Slide 18: Effect of freezing

## Slide 19
The main effect of freezing on food quality is damage caused to cells by ice crystal growth.
Freezing causes
1-changes to pigments, flavours or nutritionally important components,
2- although these may be lost in preparation procedures or deteriorate later during frozen storage

## Slide 20
Food emulsions can be destabilized by freezing, and proteins are sometimes precipitated from solution
prevents use of frozen milk. In baked goods a high proportion of amyl pectin is needed in the starch to prevent retro gradation and staling during slow
freezing and frozen storage.
There are important differences in resistance to freezing damage between animal and plant tissues.
Meats have a more flexible fibrous structure which separates during freezing instead of breaking, and the texture is not damaged.

## Slide 21
In fruits and vegetables, the more rigid cell structure may be damaged by ice crystals.
The extent of damage depends on the
1-size of the crystals
2- and hence on the rate of heat transfer
However, differences in the variety and quality of raw materials and the degree of control over pre-freezing treatments both have a greater effect on food quality than changes caused by correctly operated freezing, frozen storage and thawing procedures.

## Slide 23
influence of freezing rate on plant tissues is shown in Fig
1- During slow freezing, ice crystals grow in intercellular spaces and deform and rupture adjacent cell walls.
Ice crystals have a lower water vapour pressure than regions within the cells, and water therefore moves from the cells to the growing crystals.
Cells become dehydrated and permanently damaged by the increased solute concentration and a collapsed and deformed cell structure.
On thawing, cells do not regain their original shape and turgidity.
The food is softened and cellular material leaks out from ruptured cells called drip loss

## Slide 24
In fast freezing, smaller ice crystals form within both cells and intercellular spaces.
There is little physical damage to cells, and water vapour pressure gradients are not formed; hence there is minimal dehydration of the cells. The texture of the food is thus retained to a greater extent . However, very high freezing rates may cause stresses within some foods that result in splitting or cracking of the tissues.

## Slide 25: 2. Chilling
An-Najah National University
Faculty of Agriculture

## Slide 26: 1- Chilling
Chilling is the unit operation in which the temperature of a food is reduced to between - 1ºC and 8ºC. It is used to reduce the rate of biochemical and microbiological changes, and hence to extend the shelf life of fresh and processed foods. It causes minimal changes to sensory characteristics and nutritional properties of foods and, as a result, chilled foods are perceived by consumers as being convenient, easy to prepare, high quality and ‘healthy’, ‘natural’ and ‘fresh’.

## Slide 27
Chilling is often used in combination with other unit operations (for example fermentation or pasteurization) to extend the shelf life of mildly processed foods. There is a greater preservative effect when chilling is combined with control of the composition of the storage atmosphere than that found using either unit operation alone.

## Slide 28: Chilled foods are grouped into three categories according to their storage temperature range as follows:
1. -1ºC to +1ºC (fresh fish, meats, sausages and ground meats, smoked meats and breaded fish).
2. 0ºC to +5ºC (pasteurised canned meat, milk, cream, yoghurt, prepared salads, sandwiches, baked goods, fresh pasta, fresh soups and sauces, pizzas, pastries and unbaked dough).
3. 0ºC to +8ºC (fully cooked meats and fish pies, cooked or uncooked cured meats, butter, margarine, hard cheese, cooked rice, fruit juices and soft fruits).

## Slide 29: 2-Theory
2. 1 Fresh foods
The rate of biochemical changes caused by either micro-organisms or naturally occurring enzymes increases logarithmically with temperature. Chilling therefore reduces the rate of enzymic and microbiological change and retards respiration of fresh foods

## Slide 30: The factors that control the shelf life of fresh crops in chill storage include:
the type of food and variety or cultivar
the part of the crop selected (the fastest growing parts have the highest metabolic rates and the shortest storage lives )
the condition of the food at harvest (for example the presence of mechanical damage or microbial contamination, and the degree of maturity)
the temperature of harvest, storage, distribution and retail display
the relative humidity of the storage atmosphere, which influences dehydration losses.
To chill fresh foods it is necessary to remove both sensible heat (also known as field heat) and heat generated by respiratory activity.

## Slide 31: 2.2. Processed foods
There are four broad categories of micro-organism, based on the temperature range for growth
1. thermophilic (minimum: 30–40ºC, optimum: 55–65ºC)
2. mesophilic (minimum: 5–10ºC, optimum: 30–40ºC)
3. psychrotrophic (minimum: 0–5ºC, optimum: 20–30ºC)
4. psychrophilic (minimum: 0–5ºC, optimum: 12–18ºC).

## Slide 32
Chilling prevents the growth of thermophilic and many mesophilic micro-organisms. The main microbiological concerns with chilled foods are a number of pathogens that can grow during extended refrigerated storage below 5ºC, or as a result of any increase in temperature (temperature abuse) and thus cause food poisoning
Examples of these pathogens that survive chilling conditions are Aeromonas hydrophilia, Listeria spp, Yersinia enterocolitica, some strains of Bacillus cereus, Vibrio parahaemolyticus and enteropathogenic Escherichia coli (Marth, 1998). An example of the last (E.coli 0157:H7) may cause hemorrhagic colitis after ingestion of as little as ten cell

## Slide 33: The shelf life of chilled processed foods is determined by:
• the type of food
• the degree of microbial destruction or enzyme inactivation achieved by the process
• control of hygiene during processing and packaging
• the barrier properties of the package
• temperatures during processing, distribution and storage.

## Slide 34: 2.3. Cook–chill systems
Individual foods (for example sliced roast meats) or complete meals are produced by cook–chill or cook–pasteurise–chill processes
These products, which include complete meals or components such as sauces, were developed for institutional catering to replace warm-holding,1 which reduces losses in nutritional and eating quality and is less expensive

## Slide 35: The range of chilled foods can be characterised by the class of microbial risk that they pose to consumers as follows:
Class 1 foods containing raw or uncooked ingredients, such as salad or cheese as ready-to-eat (RTE) foods (also includes chill-stable raw foods, such as meat, fish, etc.)
Class 2 products made from a mixture of cooked and low risk raw ingredients
Class 3 cooked products that are then packaged
Class 4 products that are cooked after packaging, including ready-to-eat-products for- extended-durability (REPFEDs) having a shelf life of 40+ days (the acronym is also used to mean refrigerated-pasteurised-foods-for-extended durability).

## Slide 36: 3- Equipment
Chilling equipment is classified by the method used to remove heat, into:
• mechanical refrigerators
• cryogenic systems: A cryogen is a refrigerant that changes phase by absorbing latent heat to cool the food. Cryogenic chillers use solid carbon dioxide, liquid carbon dioxide or liquid nitrogen. Solid carbon dioxide removes latent heat of sublimation

## Slide 37: 3.1. Control of storage conditions
In all stores it is important to maintain an adequate circulation of air using fans, to control the temperature, relative humidity or atmospheric composition. Foods are therefore stacked in ways that enable air to circulate freely around all sides. This is particularly important for respiring foods, to remove heat generated by respiration or for foods, such as cheese, in which flavour development takes place during storage. Adequate air circulation is also important when high storage humidities are used for fresh fruits and vegetables

## Slide 38: 4. Effect on foods
The most significant effect of chilling on the sensory characteristics of processed foods is hardening due to solidification of fats and oils.
enzymic browning, lipolysis, colour and flavour deterioration in some products and retrogradation of starch to cause staling of baked products
Lipid oxidation is one of the main causes of quality loss in cook–chilled products, and cooked meats in particular rapidly develop an oxidised flavour termed ‘warmed-over flavour’ (WOF),

## Slide 39
Physico-chemical changes including migration of oils from mayonnaise to cabbage in chilled coleslaw, syneresis in sauces and gravies due to changes in starch thickeners, evaporation of moisture from unpackaged chilled meats and cheeses, more rapid staling of sandwich bread at reduced temperatures and moisture migration from sandwich fillings may each result in quality deterioration

## Slide 40: 4.1. Loss of vitamins during chilling % per day.