## Slide 1: Digital Communications
  Band Pass pulse transmission
  Matched Filter
  3.1

## Slide 2: Introduction:
Source encoder compresses message to remove redundancy
Encryption protects against eavesdroppers and false messages
Channel encoder adds redundancy for error protection
Modulator converts digital inputs to signals suitable for physical channel

## Slide 3: Base band pulse transmission
Main Topics of this chapter
  The matched filter
  Calculation of the bit error rate due to the presence of channel noise
  Inter symbol interference
  Nyquist’s criteria for distortion less base band data transmission
  Correlative level coding
  Equalization
  The eye pattern

## Slide 4
Baseband Pulse Transmission (Review)
1) Digital data sources
  D/A conversion
  Discrete by nature [i.e., digital computer]
2) Baseband transmission: when no modulation is used.
3) Bandpass transmission: when modulation is used.
Digital data have a broad spectrum (wide B.W.) with a significant low frequency content.

## Slide 5
Baseband Pulse Transmission (Review)
Baseband transmission requires the use of a low – pass channel with a large B.W.
In practice the channel is dispersive [deviates from ideal] So, the received pulses are affected by adjacent pulses leading to ISI which is a major source of bit error.
Controlling the pulse shape helps correcting the ISI
AWGN is the other form of noise
ISI & AWGN appear simultaneously but will be studied separately.

## Slide 6: Baseband

## Slide 7: ISI and AWGN
When digital data are transmitted through the communication channel it will be disturbed by two different noise types
Inter-Symbol interference (ISI) which results due to the overlap between the adjacent pulses (treated by equalization)
The additive white Gaussian noise (AWGN) which can be treated by the use of the matched filter at the receiver input

## Slide 8: matched filter
Is designed to maximize the signal-to-noise ratio (SNR) of a received signal.
It is called a "matched" filter because it is designed to match the characteristics of the transmitted signal.
It is typically used in the receiver of a digital communication system to optimize the detection of the transmitted signal in the presence of noise.
It works by comparing the received signal to a reference signal that represents the expected characteristics of the transmitted signal. The reference signal is usually derived from the transmitted signal, and is called the "pulse shape" or "pulse waveform."

## Slide 9: matched filter
To maximize the SNR of the received signal, the matched filter multiplies the received signal by the conjugate of the pulse shape and integrates the result over a certain time period.
This process is known as "correlation," and it effectively filters out noise and other unwanted signals that do not match the pulse shape.
The output of the matched filter is a waveform that is a replica of the transmitted signal, but with improved SNR.

## Slide 10: MATCHED FILTERS
The matched filter is the optimal linear filter for maximizing the signal to noise ratio (SNR) in the presence of additive stochastic noise.
Matched filters are commonly used in radar, in which a signal is sent out, and we measure the reflected signals, looking for something similar to what was sent out.
Two-dimensional matched filters are commonly used in image processing, e.g., to improve SNR for X-ray pictures
The matched filter is the first element in the base band receiver
The matched filter is a linear time invariant system used to maximize the signal to noise energy of the received signal sample

## Slide 11
A basic problem that often arises in the study of communication systems is that of detecting a pulse transmitted over a channel that is corrupted by channel noise.

## Slide 12
A matched filter can be defined as follows:
A filter which immediately precedes the decision circuit in a digital communications receiver is said to be matched to a particular symbol pulse, if it maximises the output SNR at the sampling instant when that pulse is present at the filter input.

## Slide 13
The purpose of the Matched Filter circuit is to design an impulse response h(t) of the filter such that the output signal-to-noise ratio is maximized.
Let G(f) and H(f) denoted the Fourier Transform of g(t) and h(t).
Noise Power
– Since w(t) is white with a power spectral density , the spectral density function of Noise is
– The noise power is
Signal Power is

## Slide 16
Solve …
You will get

## Slide 17
The impulse response of the filter, is a time-reversed and delayed version of the input signal i.e., .
This means that the filter is matched to the input signal.
The maximum peak pulse signal to noise ratio at the sampling instant is given by .
Impulse Response of the Optimum Matched filter
Does not depend on pulse shape g(t)
Proportional to signal energy (energy per bit) Eb
Inversely proportional to power spectral density of noise

## Slide 18: Matched Filter
Detection of pulse in presence of additive noise
  Receiver knows what pulse shape it is looking for.
  Channel memory is ignored (assumed compensated by other means, e.g. channel equalizer in receiver).
Additive white Gaussian noise (AWGN) with zero mean and variance N0 /2
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period

## Slide 19: Matched Filter Derivation
Design of matched filter
  -Maximize signal power i.e. power of at t = T
  -Minimize noise i.e. power of
Combine design criteria
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period

## Slide 20: The idea

## Slide 21: Example 4.1 Matched filter for rectangular pulse
Consider the rectangular pulse shown below
  find the matched filter output.
  Show that the filter can be implemented by using an integrator followed by a sampling switch.

## Slide 22: Solution
The output signal is obtained by the convolution sum between and
is similar to the conjugate of g(t);
The resulting filter output is shown below

## Slide 23: solution
The peak value of can be obtained when which can be obtained by passing the rectangular pulse through an integrator, then sample the integrator output at