## Slide 1
Digital Communications
BER & eye diagram (eye pattern)
3.2

## Slide 2
The error rate refers to the probability that an error will occur during the transmission of data from a sender to a receiver.
An error can occur due to various factors, such as noise, interference, or signal distortion.
The error rate is often expressed as a percentage or as a ratio, and it is used to measure the performance of a communication system.
There are several different types of errors that can occur in digital communications, including:
  Bit errors: errors in which one or more bits are transmitted incorrectly
  Frame errors: errors in which an entire frame of data is transmitted incorrectly
  Symbol errors: errors in which one or more symbols (a group of bits) are transmitted incorrectly

## Slide 3
The error rate of a digital communication system can be affected by various factors, such as;
    the SNR of the received signal,
    the transmission rate, and
    the modulation scheme.
In general, higher SNR and lower transmission rates tend to result in lower error rates, while lower SNR and higher transmission rates tend to result in higher error rates.
To improve the error rate of a digital communication system, various error correction and detection techniques can be used, such as parity check, cyclic redundancy check (CRC), and forward error correction (FEC).
These techniques add redundant information to the transmitted data, which can be used to detect and correct errors that occur during transmission.

## Slide 5: Decision Theory (notation ??)

## Slide 6: Error rate due to noise
Probability of Error expression to be derived
PCM polar NRZ signaling is our reference for analysis.
The channel noise is modeled as Additive White Gaussian Noise of zero mean and power spectral density

## Slide 7: Selected Fourier transform

## Slide 8: Bit Error Rate (BER)
The receiver of the communication system can be modeled as shown below
The signaling interval will be , where is the bit duration
x(t)
y(t)
Y

## Slide 10: Bit error rate
The received signal can be given by
It is assumed that the receiver has acquired knowledge of the starting and ending times of each transmitted pulse.
The receiver has a prior knowledge of the pulse shape, but not the pulse polarity.

## Slide 11: Receiver model
The structure of the receiver used to perform this decision making process is shown below

## Slide 12: Possible errors
When the receiver detects a bit there are two possible kinds of error
Symbol 1 is chosen when a 0 was actually transmitted; we refer to this error as an error of the first kind
Symbol 0 is chosen when a 1 was actually transmitted; we refer to this error as an error of the second kind

## Slide 13: Average probability of error calculations
To determine the average probability of error, each of the above two situations will be considered separately;
1) If symbol 0 was sent then, the received signal is

## Slide 14: Average probability of error calculations
The matched filter output will be given by
The matched filter output represents a random variable

## Slide 15: Average probability of error calculations
This random variable is a Gaussian distributed variable with a mean of
The variance of is
The conditional probability density function the random variable , given that symbol 0 was sent, is therefore

## Slide 16: Average probability of error calculations
The probability density function is plotted as shown below
To compute the conditional probability, , of error that symbol 0 was sent, we need to find the area between and

## Slide 17: Average probability calculations
In mathematical notations

## Slide 18: Complementary error function
The integral
Is known as the complementary error function which can be solved by numerical integration methods
erfc(z) ≡ 1 − erf(z)

## Slide 19: Q Function
Q function
Complementary
error function erfc
Relationship
Erfc[x] in Mathematica
erfc(x) in Matlab
Probability of error exponentially decreases with SNR

## Slide 20
erfc(z) = 1-erf(z)

## Slide 21
Complementary error function

## Slide 22
error function

## Slide 23: Average probability of error in terms of
By letting , , becames

## Slide 24: : If symbol 1 is transmitted but 0 is received
2) the conditional probability density function of Y, given that symbol 1 was sent is given as
Which is plotted in the next slide
(this can be found by using the same procedure as )

## Slide 25: Propability density function
The probability density function is plotted as shown below

## Slide 26
The probability of error that symbol 1 is sent, but the received bit is mistakenly read as 0, is given by

## Slide 27
By letting , , becames

## Slide 28: Expression for the average probability of error
The average probability of error is given by

## Slide 29: Optimum threshold
In order to find the value of which minimizes the average probability of error we need to derive with respect to and then equate to zero as
From math's point of view (Leibniz’s rule)

## Slide 30: Optimum value of the threshold value
If we apply the previous rule to , then we may have the following equations
By solving the previous equation we may have

## Slide 31: Optimum value of the threshold 𝜆 value
From the previous equation, we may have the following expression for the optimum threshold point
If both symbols 0 and 1 occurs equally in the bit stream, then , then
Next slide…..

## Slide 32: Optimum value of the threshold 𝜆 value

## Slide 33: Average probability of error vs
A plot of the average probability of error as a function of the signal to noise energy is shown below

## Slide 34: approximation for large values of
As it can be seen from the previous figure, the average probability of error decreases exponential as the signal to noise energy is increased
For large values of the signal to noise energy the complementary error function can be approximated as

## Slide 35: Average probability of error for different line codes
The expression for the average probability of error depends on the line code used
For the unipolar NRZ, the average probability of error is given by

## Slide 36: Average probability of error for different line codes
For the unipolar RZ, the average probability of error is given by
The average probability of error for bipolar NRZ is given by

## Slide 37: Check this item??
Q) Which has higher error probability performance? Explanation:
A) Bipolar base-band signalling has high error probability performance than the others. (to be reviewed)

## Slide 40: Example1
Solution

## Slide 41: Example1 (solution)

## Slide 42: An eye diagram
is a graphical representation of the signal integrity of a digital communication system.
a useful tool for analyzing the performance of a communication system and identifying potential issues with the signal.
To create an eye diagram, a continuous stream of digital data is transmitted over a communication channel and then sampled at regular intervals.
The resulting samples are plotted on a graph with the x-axis representing time and the y-axis representing the signal level. The resulting plot is called an eye diagram.
An ideal eye diagram will have a clear and symmetrical "eye" shape, with the signal level remaining within a certain range around the center line.
This indicates that the signal is stable and free from noise and other disturbances.
On the other hand, if the eye diagram is distorted or has a poor "eye" shape, it may indicate that the signal is noisy or distorted, which can lead to errors in the transmitted data.

## Slide 43: An eye diagram
Eye diagrams are commonly used in the design and testing of digital communication systems to ensure that the signals are of high quality and free from noise and other distortions.
They are particularly useful for analyzing high-speed digital communication systems, where small variations in the signal can have a significant impact on the performance of the system.
In summary
an eye diagram is a graphical representation of the signal integrity of a digital communication system.
It is used to analyze the performance of the system and identify potential issues with the signal, such as noise and distortion.
Eye diagrams are commonly used in the design and testing of digital communication systems to ensure that the signals are of high quality.

## Slide 44: Eye Diagram
Eye diagram is empirical measure of signal quality
The more open the eye, the better the reception

## Slide 45
Interpretation:
Eye Width: The horizontal width of the eye opening represents the timing jitter of the signal. A wider eye opening indicates lower jitter and better timing stability.
Eye Height: The vertical height of the eye opening represents the voltage margin between different signal levels. A larger eye height indicates better signal-to-noise ratio and less distortion.
Eye Closure: The extent of overlap or closure of the eye opening indicates the presence of noise, intersymbol interference (ISI), or distortion in the signal. Higher closure implies higher levels of noise or distortion, which can degrade signal integrity and increase the bit error rate (BER).

## Slide 46: Eye Pattern -Seen in oscilloscope -The Cleaner, the better -Good indication of transmission quality

## Slide 47
what is eye diagram, when and why do we use it
An eye diagram is a graphical representation of the voltage versus time of a digital signal, used to visualize the signal's quality and integrity. It is often used to analyze the performance of a communication system, particularly in high-speed digital circuits.
An eye diagram is created by superimposing a series of oscilloscope traces of a digital signal, with each trace representing a single-bit period. The resulting pattern, resembling an eye, allows engineers to quickly assess the signal's quality and identify any potential issues, such as jitter, noise, or signal distortion.
Eye diagrams are used in a variety of applications, including testing and debugging high-speed communication systems, analyzing the performance of data links and networks, and verifying compliance with industry standards. They are an essential tool for ensuring the reliable and efficient transmission of data in modern digital systems.

## Slide 48
The End