## Slide 1
  Digital Communications
  Digital Modulation (intro)
  4

## Slide 2: What makes a Communication System GOOD
We can measure the “GOODNESS” of a communication system as:
How close is the estimate to the original signal m(t)
  Better estimate = higher quality transmission
  Signal to Noise Ratio (SNR) for analog m(t)
  Bit Error Rate (BER) for digital m(t)
How much power is required to transmit s(t)?
  Lower power = longer battery life, less interference
How much bandwidth B is required to transmit s(t)?
  Less B means more users can share the channel
  Exception: Spread Spectrum -- users use same B.
How much information is transmitted?
  In analog systems information is related to B of m(t).
  In digital systems information is expressed in bits/sec.

## Slide 3: What is modulation
Modulation is the process of encoding information from a message source in a manner suitable for transmission
It involves translating a baseband message signal to a bandpass signal at frequencies that are very high compared to the baseband frequency.
Baseband signal is called modulating signal
Bandpass signal is called modulated signal

## Slide 4: Modulation Techniques
Modulation can be done by varying the
  Amplitude
  Phase, or
  Frequency
  of a high frequency carrier in accordance with the amplitude of the message signal.
Demodulation is the inverse operation: extracting the baseband message from the carrier so that it may be processed at the receiver.

## Slide 5: Analog & Digital Modulation
Analog Modulation
  The input is a continuous signal
  Used in first-generation mobile radio systems such as AMPS in the USA.
Digital Modulation
  The input is digital.
  Used in current and future mobile radio systems (GSM).

## Slide 6: A/D and D/A Conversion
Digital data is to be carried on an analog signal.
There are several reasons why A/D conversion is important:
Digital signals are easier to manipulate (store, transmit, and process than analog signals. This is because digital signals are discrete and can be represented with a finite number of bits, while analog signals are continuous and require an infinite number of bits to represent accurately.
Digital signals are less susceptible to noise and interference than analog signals. This is because digital signals are either on or off, and any noise or interference is less likely to affect the signal in a meaningful way.
Digital signals can be more accurate and precise than analog signals. This is because digital signals can be represented with a high degree of accuracy, while analog signals are subject to various sources of error and distortion.

## Slide 7: The main advantages of digital modulation
Improved spectral efficiency: Digital modulation schemes can pack more data into a given frequency band compared to analog modulation schemes. This means that digital systems can transmit more information in a given amount of bandwidth, which is useful in situations where the available bandwidth is limited.
Increased resistance to interference: Digital signals are more resistant to interference than analog signals. This is because any noise that is present in the signal is more likely to affect an analog signal, while a digital signal can often still be accurately recovered even in the presence of noise.

## Slide 8: The main advantages of digital modulation
Improved signal-to-noise ratio: Digital modulation schemes often have a higher signal-to-noise ratio than analog modulation schemes. This means that the signal-to-noise ratio of a digital system can be higher at the receiver, leading to improved performance.
Ease of implementation: Digital signals can be easily generated, processed, and transmitted using digital circuits, which are widely available and relatively inexpensive.
Improved security: Digital signals can be encrypted to provide confidentiality, which is not possible with analog signals.
Better quality: Digital signals can be transmitted without degradation of the signal quality, while analog signals can be subject to degradation due to noise and other factors.

## Slide 9
Tomasi
In Digital Modulation, the known analog modulation methods (i.e., AM, FM, PM) are replaced by Digital Modulation (i.e., ASK, FSK, PSK)
Digital communication systems are;
  Easy for process.
  Easy for multiplexing.
  Noise immunity .
Analog Or digital signal
Destination
Channel

## Slide 10: Shift Keying

## Slide 11: THREE basic binary modulation schemes
FSK & PSK signals have a constant envelope, so they are preferred to ASK signals for passband data transmission over nonlinear channels.

## Slide 12
Phase–recovery circuit: ensures that the oscillator supplying the locally generated carrier wave in the receiver is synchronized to the oscillator at the transmitter (frequency and phase).
coherent digital modulation: If the receiver has a phase-recovery circuit.
non-coherent: If the receiver has no phase-recovery circuit.

## Slide 13
Give examples where digital modulation techniques are used

## Slide 14
1) In digital radio the modulating signals are digital pulses but the carrier signals are analog ones.
(i.e., digital pulses modulate analog carrier).
2) Different modulation techniques are used in digital radio (ASK, FSK,…).
digital radio uses analog carriers to represent digital data.
In a non-coherent FSK scheme, when we change from one frequency to the other, we do not adhere (we do not stick) to the current phase of the signal
In coherent FSK, the switch from one frequency signal to the other only occurs at the same phase in the signal.
Digital Radio vs. Analog Radio (ASK,…)

## Slide 15
Figure. Digital data over analog carrier

## Slide 16
Figure. Types of digital modulation

## Slide 17: note
Bit rate, N, is the number of bits per second (bps).
Baud rate (Symbol rate) is the number of signal elements per second (bauds).
In the analog transmission of digital data, the signal or baud rate (S) is less than or equal to the bit rate (N).
S=N/r bauds
Where r is the number of data bits per signal element (i.e., # of bits/sample?).
or
bit rate=r* baud rate

## Slide 18: example
An analog signal carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.
Solution
Note: signal element (also called symbol or sample)
r= 4 bits/symbol,
S= 1000 symbols/second, and
N (bit rate) is unknown.
(Bit rate) N = r*S = 4 bits/symbol * 1000 symbols/second
= 4000 bps

## Slide 19: example
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud.
-How many data elements are carried by each signal element?
-How many signal elements do we need?
Solution
-Given: N=8000 bps (bit rate), S = 1000 (baud rate or symbol rate).
-But both r and L are unknown. (r is # of bits per baud and L is # of levels)
1) r =N/S, 8000/1000=8 bits/baud
2) L (signal elements), L=2^r=2^8=256

## Slide 20
Shannon Limit for Information Capacity
C=B log (1+S/N) bits/sec .
C represents the number of independent symbols that can be carried out through the system in a given time.
C=B log (1+SNR) =3.32 B log (1+ SNR).
2
2
10
Example : Consider a standard voice-band communication channel with SNR of 1000 (30 dB) and a bandwidth of 2.7 kHz . Find the channel capacity.
Solution :
C=B log (1+SNR)=(2. 7K) log (1+1000) C= 26.9 kbps
The 2.7kHz bandwidth will carry 26.9 kbps. (this can not be done with a binary system. Hence, M-ary is needed )
2
2

## Slide 21
2.7 kHz bandwidth gives 27 kbps capacity.
Hence, each transmitted system must contain more thane one bit of information.
To achieve the Shannon limit (C) then digital transmission systems that have more than two output conditions (symbols) must be used.
It is the way that we use the channel which will enable us to use 27kHz channel capacity.
Shannon Limit for Information Capacity
Example : BW=2.7kHz.
Solution : C=27kHz.
Comments:

## Slide 22
M- ARY Encoding
Binary FSK & binary PSK are binary systems (only two possible output 0, 1).
- BFSK & BPSK are M-ary systems with M=2 .
- it is better to encode at a level higher than binary ( M>2 ).
N = log M N: #of bits needed per symbol
M: # of output possible conditions with N bits
2
Input
output
Modulation
If 2-bits were allowed to enter a modulator before the output were allowed to change ,
2 = log M & M = 2 =4
2-bits
2
2
1
2
3
4
4- different
Output conditions.
N=1 M=2 = 2
N=2 M=2 = 4
N=3 M=2 = 8
3
1
2

## Slide 23: Bit rate vs. Baud rate (symbol rate)

## Slide 24: 1) Nyquist rate, fs>2W 2) Bitrate vs. BW & # of levels 3) BW vs. bitrate & # of levels 4) BW vs. bitrate & # of bits /symbol

## Slide 26
Amplitude Shift Keying – ASK On-Off Keying
For AM V(t) = A/2 [1+ m(t)] cos ( 2* pi * fc*t).
modulating signal carrier signal
Let m(t)=+1 (binary) on – off-keying . (A cos(2*pi*fc*t) OR zero
OOK modulation .
V(t) = Am(t) cos(2*pi*fc*t). If m(t) = 0 or 1 ook
Double side band
_
dsb
DSB
OOK
carrier

## Slide 27: Amplitude Shift Keying (ASK)
ASK: changing the amplitude of a carrier signal to reflect the amplitude levels in the digital signal.
For example: a digital “1” could not affect the carrier signal, whereas a digital “0” would, by making it zero.
The line encoding will determine the values of the analog waveform to reflect the digital data being carried.

## Slide 28: Figure. Implementation of binary ASK (on-off keying, - OOK)

## Slide 29: Bandwidth of ASK
The bandwidth B of ASK is proportional to the signal rate S.
B = (1+d)S
“d” is due to modulation and filtering, 0<d<1
Figure. Binary amplitude shift keying (symbol, element or baud rate)

## Slide 30: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using ASK with d = 1?
Solution
Note: r=1 for BASK
fc = 250kHz., as the middle of the bandwidth (200-300).
B=100kHz. (which is 300-200)
B=(1+d)S  B=(1+1)S B=2S symbols/sec,
then, S=50k
S=N/r  N=S*r=50*1,  N=50 kbps
Bit rate = BW/2 (for BASK)

## Slide 31: Simply
For (BASK), the bandwidth required is approximately equal to the data rate.
For example, if the data rate is 1000 (bps), the bandwidth required for BASK would be approximately 1000 Hz.

## Slide 32: Example/ full-duplex
We normally use full-duplex links (both directions).
We divide the bandwidth into two bands each with a carrier frequency, as shown in the figure below.
It shows the positions of the two carrier frequencies and the bandwidths.
The available bandwidth for each direction is now 50 kHz,
The data rate is 25kbps in each direction. (as seen in the previous example)
Figure. Bandwidth of full-duplex ASK

## Slide 33
The digital data stream changes the frequency of the carrier signal, fc.
For example,
  “1” is represented by f1=fc +f,
  “0” is represented by f2=fc-f.
Frequency Shift Keying-FSK
Two different frequencies

## Slide 34: Bandwidth of FSK
If the difference between the two frequencies (f1 and f2) is 2f, then the required bandwidth (B) will be:
B = (1+d)xS +2f
Fig. BFSK

## Slide 35: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulate this data using FSK with d = 1?
Solution
fc=250kHz. The midpoint of the band (200 to 300).
B=300-200 =100 kHz
B=(1+d)S+2Δf=2S+2Δf=100,
OR, from Figure, 2Δf=2S, Δf=S
But, B=4Δf (no guard period).
 2S+2Δf=100 4S=100 s=25kbps

## Slide 36: Multi Level FSK
Similarly to ASK, the FSK can use multiple bits per signal element.
That means we need to provision for multiple frequencies, each one to represent a group of data bits.
The bandwidth for FSK can be higher
B = (1+d)xS + (L-1)/2f
= LxS
Figure. Bandwidth of MFSK used in a previous Example

## Slide 37
More than two frequencies are used
More bandwidth efficiency but more susceptible to error

## Slide 38: Example A
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.
Solution:
-L = 23 = 8 (# of levels). S=N/r bauds
-The baud rate is S =bit rate/#of bits per symbol)
-So, S= 3 Mbps/3 bits per symbol  S=1 Mbaud.
-This means that the carrier frequencies must be 1 MHz apart (2Δf = 1 MHz).
-The bandwidth is B=LxS= 8 × 1M = 8MHz.
-Fig. A shows the allocation of frequencies and bandwidth.

## Slide 39
Solution (summary)
L= 8. (# of levels 8 carriers).
S = 3 Mbps  1 Mbaud.
fc = 1 MHz apart (2Δf = 1 MHz around each sub carrier).
bandwidth (B=LxS)  B = 8 × 1M = 8MHz.
Fig.A shows the allocation of frequencies and bandwidth.
Fig.A Bandwidth of MFSK used in Example A
What is the BW of each symbol?
What is the total BW required?

## Slide 40
Frequency Shift Keying - FSK
v(t) = Vc cos [(wc +( Vm (t) w )/2)t ]
v(t): binary FSK waveform .
Vc: peak unmodulated carrier amplitude.
wc: radian carrier frequency .
Vm(t): binary digital modulating signal.
w : change in radian output frequency .
Binary input
Analog output
0
1
0
1
fs
fm
fs
fm
Other form to present FSK

## Slide 41
fs : space frequency .
fm :mark frequency .
Time
freq
fm
fs
Binary FSK
fm > fs

## Slide 42
Bandwidth Consideration of FSK
Binary input
Analog output
FSK modulator (VCO)
1
0
1
0
1
0
0
1
1
0
0
0
1
0
T1
2T1
fa=fb/2
f=fb/4
tb
Highest fundamental frequency
Occurs when alternative 1/0 .
fb is the input bit rate AND fa is the baud (output) rate

## Slide 43
fb : input bit rate (bps).
tb : time of one bit = 1/fb .
T1 : period of shortest cycle .
1/T1 : fundamental frequency of binary, square wave.
Fastest input rate when the input is a series of alternating 1s & 0s.(square wave) .
Highest modulating frequency = 0.5 input rate
(i.e., output frequency fa = fb/2).

## Slide 44
1
1
1
0
tb
2 f
1/2tb
fc
fs=fc- f
fm=fc+ f
Carrier freq
FSK
modulator
Peak frequency deviation D f
f =abs(fm – fs) /2 = 1/4tb (Hz. minimum )
fs = fc -Df = fc – 1/4tb
fm = fc + Df = fc+ 1/4tb
For FSK :
B.W=( fm+ 1/tb) – (fs – 1/tb) = fm – fs +2/tb = 2( f + 1/tb ).
B.W=2(Df+ 1/tb)
1/tb
fs – 1/tb
fc
1/tb
fs
fm
fm+1/tb
FSK frequency spectrum (pulse sinusoidal wave have freq. spectrum that is ((sin x)/x)
B = (1+d)xS +2f

## Slide 45
Example:
Determine the bandwidth & baud for an FSK signal with a mark frequency of 51 kHz, a space frequency of 49 kHz , and a bit of 2 kbps.
Solution :
B.W = fm – fs +2/tb = 2(Df+1/tb). OR BW=fm-fs+2fb (Note: 1/tb =bit rate?)
1) B.W = fm – fs + 2/tb  fm – fs + 2fb
B.W= 51000 – 49000+2(2000) = 6000Hz.
>>> tb= 1/fb = 1/2000 = 0.5 msec.
B.W= 51000 – 49000+2/(0.5*10^-3) = 6000Hz .
2) With BFSK (r=1),
baud = input bit rate =2000 bits/sec

## Slide 46
-
+
Data output
FSK
Input
BPF
BPF
Envelop detector
Envelop detector
-
+
FSK
input
Data output
BPF
BPF
carrier
carrier
Non coherent FSK demodulator
coherent FSK demodulator
FSK Receiver
fs
fm

## Slide 47
amp
VCO
Phase compensator
Dc-error voltage
Analog FSK in
d
Binary data output
PLL
fs
fm
+V
0V
-V
Fig. PLL-FSK demodulator (most common)
Phase Locked Loop

## Slide 48: PLL
PLL is a control system that generates an output signal whose phase is related to the phase of an input reference signal.
It consists of a voltage-controlled oscillator (VCO), a phase comparator, and a feedback loop.
The VCO generates an output signal with a frequency that can be varied by applying a control voltage.
The phase comparator compares the phase of the VCO output signal with the phase of the reference signal and generates an error signal based on the difference between the two phases.
This error signal is used to control the VCO, causing its frequency to change so that the phase of its output signal is locked to the phase of the reference signal.
PLLs are commonly used in a variety of applications, including frequency synthesis, clock and data recovery, and control systems.
They are useful because they can generate stable, precise output signals even when the reference signal is noisy or unstable.

## Slide 49
Minimum Shift –Keying (MSK) -MFSK
Similar to FSK but
fm & fs = n (fb / 2) , (n is odd)
fs & fb = n fb /n , (n is odd)
Phase discontinuties
fs = n (fb /2)
Sudden change in frequency, phase ??
This may create problems error
Fig . Non continuous FSK waveform (not MSK )
MSK is a form of continues – phase Frequency Shift Keying (CPFSK)

## Slide 50
Logic 1
Logic 0
Smooth continuoes transition
fm
fs
fb = 1kbps
MSK
Fig . Continuous-phase MSK waveform .( error is less)
fm : mark frequency .
fm = 5 (fb /2) = 5*1000/ 2 =2500 Hz.
fs = 3 (fb / 2) = 3*1000 /2 = 1500Hz.

## Slide 51
Binary Phase Shift Keying (BPSK).
Analog input
Binary digital signal
PM
PSK
Limited number of output phases
Binary PSK (BPSK) two phases
also called phase reversal keying (PRK)
or, pi phase modulation ( ) ?
1
0
1
Time
Time
tb
Binary input
BPSK
Output
Degree 0 180 0 180
Radian 0 pi 0 pi
Sin wc t
-Sin wc t
Sin wc t
-Sin wc t

## Slide 52
BPSK Transmitter
OUT PUT IS THE PRODUCT X.Y
+1V
-1V
Balanced (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0
FIG. Simplified block diagram of a BPSK Tx (Modulator).

## Slide 53
BPSK Receiver
Coherent
Carrier
Recovery
BPSK input
Balanced
Modulator
(multipler)
LPF
Binary data out
Logic +1
Tx
+sin(wc t)
Logic 0
-sin(wc t)
FIG . BPSK R x
Tx
+sin(wc t)
AND -sin(wc t)
+ 0.5
Logic 1
+sin(wc t)
-
X
fcut <<2wc
BPSK
MOD
BPSK
MOD
- 0.5
Logic 0
Demo
Demo
Rx
Rx

## Slide 54
At point X ():the output of the multiplier)
sin wc t . sin wc t out put of balanced mod.
Out 1 = sin wc t =0.5 (1-cos2wc t ) = 0.5 1. this is due to 1
Out 0 = -sin wc t = -0.5 (1-cos 2wc t )= -0.5 0 . This is due to 0
Filtered by the LPF
Filtered by the LPF
2
2

## Slide 55: PSK- Bandwidth consideration
We vary the phase shift of the carrier signal to represent digital data.
The bandwidth requirement, B is:
B = (1+d)xS
PSK is much more robust than ASK (i.e., noise is AWGN)
Figure. Binary phase shift keying

## Slide 56: Figure. Implementation of BPSK

## Slide 57: Bandwidth Consideration of BPSK (another way)
out put = sin(wa t) sin(wc t)
= 0.5 cos(wc – wa)t – 0.5 cos(wc+wa)t .
Widest output BW occurs when the input binary data are alternating.
The fundamental frequency (fa) of an alternating 1/0 bit sequence is fa=fb/2
Fundamental
Frequency of binary modulating signal
Un -modulated carrier
+1V
-1V
Balance (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0

## Slide 58
The minimum double-side Nyquist bandwidth (f N ) is
+1V
-1V
Balance (product) modulator
Reference carrier oscillator
BPF
Analog PSK output
Binary data in
X
Y
X.Y
1
0
Band width =input bit rate
=(1+d)S where d=0

## Slide 59
1
0
1
Time
Time
tb
Binary input
BPSK
Output
Degree 0 180 0 180
Radian 0 pi 0 pi
Sin wc t
-Sin wc t
Sin wc t
-Sin wc t
FIG. output phase vs. time for BPSK modulation
Figure Binary phase shift keying

## Slide 60
Example:
For a BPSK modulator with a carrier frequency of 70 MHz & an input bit rate of 10 Mbps. Determine the maximum & minimum upper & lower side frequencies , draw the output spectrum. Determine the minimum Nyquist bandwidth and calculate the baud.
Solution :
Output spectrum
fc is suppressed .
B.W=10MHz
65 fc=70 75

## Slide 61
End of section 1