## Slide 1: Digital Modulation M-ary,… 5
Digital Communications
DRAFT

## Slide 2: Quadrature PSK
To increase the bit rate, we can code 2 or more bits onto one signal element.
In QPSK, we parallelize the bit stream so that every two incoming bits are split up and PSKing a carrier frequency. One carrier frequency is phase shifted 90o from the other - in quadrature.
The two PSKed signals are then added to produce one of 4 signal elements. L = 4 here.

## Slide 3
Fig. QPSK and its implementation

## Slide 4
Quaternary Phase Shift Keying (QPSK)  M=4
QPSK: one carrier & 4 different phases (same amplitude??).
2-bits,
4 input conditions
4 output phases
QPSK
M = 2 = 2 = 4
dibits 2-bits groups .
2-bits input generate 1 output out of 4 possible output phases .
Baud rate = 0.5 input rate . (for QPSK).
baud rate = bit rate for BPSK.
What about baud rate for 8PSK, 16PSK,....
N
2

## Slide 5
Quadrature amplitude modulation is a combination of ASK and PSK.
Note

## Slide 6: example
Find the bandwidth for a signal transmitting at 12 Mbps for QPSK. The value of d = 0.
Solution
For QPSK, 2-bits is carried by one signal element (one baud).
Then, r = 2, N=12Mbps.
the signal rate (baud rate) is S = N/r =12/2= 6 Mbaud.
Band width, B=(1+d)S=(1+0)S, then B=6MHz.

## Slide 7
QPSK transmitter

## Slide 8
2-bits are serially input then we have only 1 output.
So, rate of change at the output = half that of the input rate.
QPSK 2 - BPSK Combined in parallel.
Possible outputs are
+sin wc t + cos wc t
+sin wc t - cos wc t
-sin wc t + cos wc t
-sin wc t - cos wc t

## Slide 9
Example:
For the QPSK modulator, construct the truth table, phasor diagram and constellation diagram.
Solution :
For Q=0 , I=0
I-ch balanced modulator output is -sin wc t
Q-ch balanced modulator output is -cos wc t
Output of the linear summer is -sinwc t – cos wc t
Out put due to (0,0) is 1+1 tan (-1) = 2 -135 (Q I = 0 0)
= 1.414 sin (wc t – 135 ) .
-1
QPSK TRUTH TABLE
Similarly

## Slide 10: Constellation diagram
A constellation diagram helps us to define the amplitude and phase of a signal when we are using two carriers, one in quadrature of the other.
The X-axis represents the in-phase carrier and the Y-axis represents quadrature carrier.

## Slide 11
Fig. constellation diagram
Fig. phasor diagram
All have same amplitude
Fig. output phases –versus-time relation ship for a QPSK modulator

## Slide 12
Figure Constellation diagrams for some QAMs

## Slide 13
Notes on QPSK
1) All QPSK outputs have the same amplitude.
2) angular separation between any two adjacent phasors in QPSK is 90 degree then we can correct up to ± 45 shift in phase

## Slide 14
Bandwidth Consideration for QPSK (option 2)
I-ch fb/2 & TbI =2Tb
input data fb b/s
Q-ch fb/2 & TbQ =2Tb
Stretching bit
B.W Compression
Input data is divided into two channels
I-ch
fb/2
fb/2 Q-ch
Binary input data fb
Q I
Balanced modulator
Balanced modulator
+1
+1
_
_
Sinwc t
coswc t
+Sinwc t
+coswc t
-
-

## Slide 15
FIG. B.W consideration of a QPSK modulator.
The bit stretched to twice the input bit length. (B.W=1/T; as T increases then B.W decreases)
Baud rate: fastest output rate of change =0.5 input bit rate for (QPSK).
=same input bit rate for (BPSK)
I –ch
fb/2
Q –ch
fb/2
Input data fb

## Slide 16
The output of the balanced modulator (for QPSK) is
B.W = fb/2 for QPSK
B.W = fb for BPSK
fb/2
fc
fc – fb/4
fc +fb/4

## Slide 17
Example:
For a QPSK Modulator with an input data rate (fb) equal to 10 Mbps and a carrier frequency (fc) of 70 MHz , determine
1) the minimum double – sided Nyquist bandwidth (fN) and baud rate.
2) Compare the results with a BPSK (same conditions, previous example).
Solution :
The bit rate in both the I and Q channels is one half of the transmission bit rate.
highest fundamental frequency presented to either balanced modulator is
Input rate fa (bps)
Sin (2*pi*fc*t)
sin (2*pi*fa*t) Sin (2*pi*fc*t)
Balanced modulator

## Slide 18
The output wave from each balanced modulator is
Minimum Nyquist bandwidth is B=(72.5 – 67.5) = 5 MHz.
The symbol rate = Bandwidth, thus Symbol rate = 5M baud
B.W = 5MH z
67.5MHz
72.5MHz
fc

## Slide 19
Comparing QPSK to BPSK for the same input rate:
QPSK BPSK
(fN) 5 MHz 10 MHz
baud rate 5 M baud 10 M baud
For the same input bit rate
f N for (QPSK) =0.5 (fN) for (BPSK) f N = fb for BPSK
f N =0.5 fb for QPSK
baud rate for (QPSK) = 0.5 baud rate for (BPSK)

## Slide 20
QPSK receiver
BPF
LPF
LPF
Q I
Product detector
Product detector
Carrier recovery sin wc t
+90
Power splitter
I – CH
Q – CH
-Sin wc t + cos wc t
-Sin wc t + cos wc t
-Sin wc t + cos wc t
Sin wc t
cos wc t
Cos(wc t)(-sin wc t +cos wc t)
sin(wc t)(-sin wc t +cos wc t)
Input QPSK signal
Recived binary data
+ 0.5 V (logic 1)
+ 0.5 V (logic 0)
-
-

## Slide 21
Now, for the input –sin wct +cos wct (coming from QI=10), then
Similarly, Q = 0.5 V  Q=1 (logic).

## Slide 22
Offset QPSK (OQPSK) OR (OKQPSK) k: KEYD
One half bit delay
Reference carrier oscillator
Balance modulator
+90
Balance modulator
Linear summer
Fig. OQPSK block diagram
I –ch input data
OQPSK OUT
OQPSK OR OKQPSK is a modified form of QPSK where the bit waveforms on the I & Q channels are offset or shifted in phase from each other by one-half of bit time .
Q –ch input data

## Slide 23
Q-channel starts half bit duration after I-channel starts
Fig. bit alignment.
I-ch
Q-ch
tb
tb/2
b0
b1
b2
b3
b0
b1
b2
b3
tb
FIG. Constellation

## Slide 24
In OQPSK :
There is never more than a single bit change in the dibit code ,
So; There is never more than a 90 shift in the output phase.
In conventional QPSK 00 to 11 (the two bits changed) then we may have 180 shift in the output phase .
similarly 01 to 10 the two bits changed??
An advantage of OQPSK is the limited phase shift .
A disadvantage of OQPSK is that changes in the output phase occurs at twice the data rate in I, Q channels
baud (OQPSK) =2 baud (QPSK)
B min is ; fN (OQPSK) =2 fN (QPSK)

## Slide 25
Eight – Phase PSK
8- PSK = M-PSK, where M=8 or N-3
Binary M =2 N = 1
Dibit M =4 N =2
Tribit M=8 N=3

## Slide 26
Reference oscillator
Product modulator
+90
product modulator
Linear summer
Fig. 8-PSK modulator
8-PSK
PAM
PAM
sin wc t
cos wc t
M-ary pulse amplitued modulation
M=4
2to4 level converter
2to4 level converter
C
Inverter
C
Q I C
Q-channel
I-channel
fb/3
fb/3
fb/3
Input fb
+1.307
+0.541
- 0.541
-1.307
PAM levels

## Slide 27
8- PSK (M- ary M = 8 )
8 = 2 ^ 3 the incoming bits are grouped into 3 bits (tribit) .
I =In-phase channel .
Q =in- quadrature channel .
C = control channel .
Q I C
Input data fb
fb/3
fb/3
fb/3
I-channel
Q-channel
Serial to parallel converter

## Slide 28
The 2 – to – 4 level converter has 2 inputs (I , C or Q , Cpar ) AND 4 – outputs.
  parallel input digital – to-analog converter
  DACs with 2-input bits ,4-output level voltage .

## Slide 29
Reference oscillator
Product modulator
+90
product modulator
Linear summer
PAM
PAM
sin wc t
cos wc t
2to4 level converter
2to4 level converter
Q I C
Q-ch
I-ch
0
0
0 0 0
0
1
Example: For a tribit of Q=0, I=0 And C=0 (QIC=0 0 0 ), determine the output phase for the 8-PSK Modulator?

## Slide 30
Solution:
I-ch: Inputs to the 2-to-4 converter are (IC=0 0),  from truth table PAM=-0.541 V.
Q-ch: Inputs to 2-to-4 converter are (QC= 0 1 ),  from truth table PAM = -1.307 V .
`
-0.541 V
-0.541 sinwc t
Product
Mod. I
Product mod .Q
-1.307 V
-1.307 coswc t V
Coswc t
sinwc t
Linear summer output = -0.541 sin wc t -1.307cos wc t .
= 1.41 sin(wc t – 112.5 ).
For the remaining tribit codes (001, 010 , 011 , 100 ,101 , 110 , 111) the procedure is the same .
I-ch. Product modulator

## Slide 31
Here, only one bit changes between any two adjacent phases, this is called Gray Code or Maximum distance code. This is used to reduce the number of transmission errors .
Fig. Phaser diagram.
Fig. Constellation

## Slide 32
Truth table for 8-PSK modulator
Binary input 8-psk output phase
000 -112.5
001 -157.5
010 -67.5
011 -22.5
100 +112.5
101 +157.5
110 +67.5
111 +22.5
Cos wc t
sin wc t
110
100
101
011
010
000
001
111
QI C
Angular separation between any two adjacent phasors is 45. (i.e., half that of QPSK).
So, an 8-PSK signal can undergoes almost ±22.5 phase shift during transmission & still retain its integrity.
Here, only one bit changes between any two adjacent phases, this is called Gray Code or Maximum distance code. This is used to reduce the number of transmission errors .

## Slide 34
Baud rate for 8-PSK is (1/3)fb =minimum band width
Power splitter splits the I,C,Q to three times the input

## Slide 35: note-34
Slide 49

## Slide 36
68.333
71.667
B=3.333MHz
fc =70
Example: For an 8 – PSK modulator with an input data rate fb = 10 Mbps and a carrier frequency of 70 MHz., determine the minimum double-sided Nyquist bandwidth (f N ) & the baud.
Solution :

## Slide 37
8 – PSK Receiver
Q I C
Q
C
I
C
Product detector
Product detector
Power splitter
Carrier recovery
90
Analog to Digital
sinwc t
Coswc t
4-level
PAM
4-level
PAM
Analog to Digital
8-PSK in
output
Parallel to serial converter
BPF

## Slide 38
16- PSK … … quadbit (M=16, N=4)
minimum bandwidth and baud =(fb/4)
What is the truth table and constellation
Find a block diagram for 16 PSK

## Slide 39
Quadrature Amplitude Modulation (QAM)
Information is contained in both the amplitude & phase of the transmitted carrier.
Both ASK and PSK are combined.
111
110
010
101
100
001
000
011
Phasor diagram
sinwc t
coswc t
Constellation diagram

## Slide 40
Reference oscillator
Product modulator
+90
product modulator
Linear summer
8-QAM
output
PAM
PAM
sin wc t
cos wc t
2 to4 level converter
2to4 level converter
C
Q I C
Q-channel
I-channel
fb/3
fb/3
fb/3
Input fb
8-QAM modulator
Adding an inverter to 8-QAM transmitter makes it an 8-PSK
I & Q bits determine the polarity of the QAM signal & the C channel determines the magnitude .
Fig. 8 –QAM Tx is so similar to the 8-PSK Tx except the inverter is removed .

## Slide 41
B.W of 8-QAM = B.W of 8-PSK =fb/3 .
Also 16-QAM …
What about 16-PSK???
I & Q bits determine the polarity of the PAM signal at the out put of the 2-to- 4 level converter, C channel determines the magnitude.
The minimum B.W required for 8-QAM is fb/3 (same as 8-PSK ).
111
110
010
101
100
001
000
011
sinwc t
coswc t
0.766v
Fig. Constellation diagram for QAM

## Slide 42
Example: For a tribit of (IQC= 000) , determine the output amplitude & phase for the 8-QAM Transmitter .
Solution :
The input to the I-ch 2-to-4 level converter are (I=0 , C=0), from I truth table, the output is -0.541
Similarly for Q-ch 0 0  2-to-4 output is - 0.541
I-ch product modulator  -.541 and sinwc t
The output is
I = - 0.541 sinwc t
Similarly; Q = - 0.541 coswc t
Output = sum ( I + Q )  - 0.541 sinwct – 0.541 coswct
= 0.765 sin(wc t -135 )
Similar procedure for 001,010,011,100,101,110,111
000 001 010 011
0.765 1.848 0.765
-135 -135 -45

## Slide 43
Truth table for the I&Q channel 2-to-4 level converter
2 Amplitudes & 4 phases
Similar procedure for 001,010,011,100,101,110,111

## Slide 44: Band width Consideration of 8-QAM & 16-QAM. Is it the same as 8-PSK and 16-PSK?

## Slide 45: 8-QAM and 16-QAM Tx & Rx

## Slide 48
Band Width Effecting (called information density )
Compares the performance of one digital technique to another.
B.W efficiency = [transmission rate(bps) / minimum bandwidth(Hz)], the unit [(bits/sec)/Hz] = bits/cycle
Bɳ

## Slide 49
Example:
Determine the bandwidth efficiencies for the following modulation schemes, BPSK,QPSK ,8-PSK & 16-PSK, for a transmission rate of 10 Mbps .
Solution :
The minimum bandwidths required are;
Modulation scheme minimum B.W (MHz) B.W efficiency
BPSK fb (FULL) =10MHz 10Mbps/10MHz =1bit/cycle
QPSK fb/2 = 5MHz 10 /5 =2 bit/cycle .
8-PSK fb/3 =3.33 MHz 10/3.33= 3 bit/cycle .
16-PSK fb/4 = 2.5 MHz 10/2.5 =4 bit/cycle .
BPSK is the least efficient.
16 PSK is the most efficient.
16-PSK requires (1/4) BW as BPSK for the same input bit rate.
Bɳ

## Slide 50: Bandwidth Efficiency
Notes: From Shannon Theorem

## Slide 51: Comparison of Modulation Types
Modulation Format | Bandwidth efficiency C/B | Log2(C/B) | Error-free Eb/N0
16 PSK | 4 | 2 | 18dB
16 QAM | 4 | 2 | 15dB
8 PSK | 3 | 1.6 | 14.5dB
4 PSK | 2 | 1 | 10dB
4 QAM | 2 | 1 | 10dB
BFSK | 1 | 0 | 13dB
BPSK | 1 | 0 | 10.5dB

## Slide 53: Spectral Efficiencies - Examples
GSM Europe Digital Cellular
  Data Rate = 270kb/s; Bandwidth = 200kHz
  Bandwidth efficiency = 270/200 = 1.35bits/sec/Hz
IS-95 North American Digital Cellular
  Data Rate = 48kb/s; Bandwidth = 30kHz
  Bandwidth efficiency = 48/30 = 1.6bits/sec/Hz

## Slide 54: Bandwidth Efficiency
GSM Europe Digital Cellular
IS-95 North American Digital Cellular

## Slide 55
SNR influences spectral efficiency.
It can be expressed as the carrier to noise power ratio (CNR).
The measure is the BER for a given CNR value.
As the noise becomes larger compared to the signal level, more errors occur.
Some modulation methods are more immune to noise than others.
Amplitude modulation methods like ASK/OOK and QAM are far more susceptible to noise so they have a higher BER for a given modulation.
Phase and frequency modulation (BPSK, FSK, etc.) fare better in a noisy environment so they require less signal power for a given noise level (Fig. ).
Performance of Digital
Modulation Techniques

## Slide 56
Performance of Digital Modulation Techniques

## Slide 57
Probability of Error & Bit Error Rate (Pe & BER)
Pe : theoretical (mathematical) expectation .
BER : empirical (historical) record .
Pe is a function of :
1) Carrier to noise power ratio (C/N) or (Eb /No) .
  Eb : average energy per bit.
  No : noise power density .
  N: thermal noise power .
  C: carrier power .
2) M: the number of possible encoding conditions .

## Slide 58
Notes: C/N
C (dBm) =10 log C(watts) /0.001.
N (dBm) = 10 log (kTB)/0.001.
Thermal Noise Power N=kTB
K=Boltzmann's constant ( 1.38 *10^ -23)J/k.
T: temperature in kelvin (0 k=-273 C) , To = 290 k, room temp .
B: bandwidth (Hz).
C/N = C/KTB (unit less) C: carrier power (W).
N: Noise power (W) .
C/N (dB) = 10 log (C/N) = 10 logC – 10 log N
= C(dBm) – N (dBm) .
dBm :…… milliwatt.

## Slide 59
Energy per bit Eb = Tb ( J/bit)
Eb : average energy per bit.
C: carrier power .
Tb: bit duration
Eb (dBJ) = 10 log Eb .
Tb = 1/Rb Rb :bit rate .
Eb = CTb = C/Rb (J/bit ) .
Eb (dBJ) = 10log (C/Rb)
=10 logC – 10 log Rb
Also ,
No =N/B (W/Hz)
No: Noise power density (W/Hz) ,
N: thermal noise power (W),
B: Bandwidth (Hz) .

## Slide 60
No(dBm) = 10 log (N/0.001) – 10 log B
No(dBm) = N(dBm) – 10log (B) .
But , No = kTB/B = KT (W/Hz) .
No(dBm) = 10 log (k/0.001) + 10 log (T) .
No : noise power present in 1Hz of Bandwidth .
Eb/No = (C/Rb)/(N/B) = CB/N Rb = (C/N) *(B/Rb)
carrier to noise power ratio noise bandwidth to bit rate ratio
Eb/No(dB) = 10 log (C/N) + 10 log (B/Rb)
Eb/No(dB) = 10 log Eb - 10 log No .
Eb/No is used to compare 2 or more digital modulation systems that use different transmission rates (bit rate ) , modulation schemes
(FSK,PSK,QAM), OR encoding techniques ( M- ary ) .

## Slide 61
Example:
For a QPSK system , C= 10^-12W , fb= 60 kbps, N = 1.2 * 10^-14 W, B= 120 kHz .
Determine
a) carrier power in dBm .
b) noise power in dBm .
c) noise power density in dBm .
d) energy per bit in dBJ .
e) carrier to noise power ratio in dB.
f) Eb/No ratio .

## Slide 62
Solution :
a) C(dBm) = 10 log C/0.001 = 10 log (1*10^-12)/0.001 = -90 dBm.
b) N(dBm) = 10 log (N)/0.001 = 10 log (1.2*10^-14) / 0.001= -109.2 dBm .
c) No(dBm) = N (dBm) - 10 log B = -109.2 – 50.79 = -160 dBm .
Or , No =N/B = 1*10^-19 then, No(dBm) = 10log (No/0.001) = -160 dBm.
d) Eb(dBJ)= 10 log C/Rb = 10 log (10^-12)/60kbps =-167.8 dBJ.
e) C/N = 10 log C/N = C(dBm) – N(dBm) = -90 – (-109.2) = 19.2 dBm .
f) Eb / No (dB) = 10 log (C/N) + 10 log (B/Rb) = 19.2 + 10 log (120 kHz/60kbps)
= 22.2 dB.
Eb/No=(C/Rb)8(B/N)= (C/N) * (B/Rb)

## Slide 63: PSK error performance

## Slide 64
Example :
Determine the minimum bandwidth required to achieve a Pe of (10^-7) for an 8-PSK system operating at 10 Mbps with a carrier-to-noise power ratio of 11.7 dB.
Solution :
From fig. 8-PSK then, Pe=10^-7  Eb/No = 14.7dB .
Eb/No = (C/Rb)/(N/B) = (C/N)* (B/Rb)  B/Rb =( Eb/No) / (C/N) .
B/Rb(dB) = ( Eb / No) (dB) – (C/N) (dB))
B/Rb = 14.7 – 11.7 = 3 dB. B/Rb = antilog 3= 2. B/Rb=2  B=2Rb
B = 2Rb  B(min) = 2(10 Mbps), B(min) = 20 MHz.

## Slide 65: QAM error performance .

## Slide 66
Example
Which system requires the highest Eb/No ratio for a probability of error of 10^-6 , a four – level QAM system or an 8-PSK system.
Solution :
From Figs.
4-QAM has Pe = 10^-6 & Eb/No =10.6 dB.
8-PSK has Pe = 10^-6 & Eb/No =14dB
For the same Pe,
Eb/No (4-QAM) < Eb/No (8-PSK) , so 4-QAM is better .

## Slide 67
Table: error performance comparison of various Digital Modulation Schemes (BER=10^-6)
Method C/N(dB) Eb/No(dB)
BPSK 10.6 10.6
QPSK 13.6 10.6
4QAM 13.6 10.6
8QAM 17.6 10.6
8PSK 18.5 14
16PSK 24.3 18.3
16QAM 20.5 14.5
32QAM 24.4 17.4
64QAM 26.6 18.8

## Slide 68
FSK Error Performance
(different than PSK ,QAM treatment ).
FSK has two types
1) Noncoherent (asynchronous ) FSK;
Tr. & Rx. are not freq or phase synchronized.
2) Coherent (synchronous) FSK;
Tr. & Rx. are in freq & phase synchronization

## Slide 69
Error rates of PSK modulation systems
Error rates of QAM modulation systems
Error rates for FSK modulation systems

## Slide 70
The End