## Slide 1: Chapter 5: Food Preservation by Heat
By: Dr. Mohmmed Sabah
Book: Food processing tecnology
2020
-Pasteurization and Heat Sterilization -Frying
An-Najah National University
Faculty of Agriculture

## Slide 2: Pasteurisation
Pasteurization: is a relatively mild heat treatment, in which food is heated to below 100 ⁰C. In low acid foods (pH>4.5, for example milk) it is used to minimize possible health hazards from pathogenic micro-organisms and to extend the shelf life of foods for several days.
In acidic foods (pH <4.5, for example bottled fruit) it is used to extend the shelf life for several months by destruction of spoilage micro-organisms (yeasts or moulds) and/or enzyme inactivation

## Slide 3
1- Three main types of pasteurization used today:
1- Lower Temperature/Longer Time (e.g. milk at 63 °C for 30 min, less often used)
2- High Temperature/Short Time (e.g. milk at 71.7 °C for 15 s)
3- Ultra High Temperature (or flash pasteurization) (e.g. Milk at 100 °C for 1-2 s

## Slide 4
The time-temperature treatment used in pasteurization depends on:
the heat resistance of the particular vegetative or pathogenic microorganisms the process is designed to destroy.
(2) the sensitivity of product quality to heat. The high-temperature and short-time (HTST) method involves a comparatively high temperature for a short time (e.g., 72 °C for 1 s for milk), whereas the low temperature and long-time procedure involves relatively low temperatures for longer times (e.g., 63 °C for 30 min for milk).

## Slide 5
Optimization of the pasteurization process depends on the relative destruction rates of organisms as compared to quality factors, but generally the HTST process results in maximum product quality.

## Slide 6
Batch Pasteurization System
Methods of Pasteurization
There are two basic methods, batch or continuous.
continuous

## Slide 7: 3. Equipment
3.1 Pasteurization of packaged foods
Some liquid foods (for example beers and fruit juices) are pasteurized after filling into containers. Hot water is normally used if the food is packaged in glass, to reduce the risk of thermal shock to the container (fracture caused by rapid changes in temperature). Maximum temperature differences between the container and water are 20 ºC for heating and 10 ºC for cooling.

## Slide 8
Metal or plastic containers are processed using steam–air mixtures or hot water as there is little risk of thermal shock. In all cases the food is cooled to approximately 40 ºC to evaporate surface water and therefore to minimize external corrosion to the container or cap, and to accelerate setting of label adhesives.

## Slide 9: Time–temperature relationships for pasteurization. The hatched area shows the range of times and temperatures used in commercial milk pasteurization.

## Slide 10: 3.2 Pasteurization of unpackaged liquids
Swept surface heat exchangers or open boiling pans are used for small-scale batch pasteurization of some liquid foods. However, the large scale pasteurization of low viscosity liquids (for example milk, milk products, fruit juices, liquid egg, beers and wines) usually employs plate heat exchangers.
Some products (for example fruit juices, wines) also require de-aeration to prevent oxidative changes during storage. They are sprayed into a vacuum chamber and dissolved air is removed by a vacuum pump, prior to pasteurization.

## Slide 11
Deaeration is the removal of air molecules (usually meaning oxygen) from another gas or liquid. It can refer to:
Use of a deaerator.
Degasification, the removal of dissolved gases, such as oxygen, from liquids.

## Slide 12
deaerator

## Slide 13
Pasteurized Foods
The most common pasteurized food is milk
Originally designed to eliminate Mycobacterium tuberculosis
Fruit juice
Spoilage yeast and bacteria, E. coli O157:H7
Beer
Spoilage bacteria and yeast

## Slide 14
Pasteurized Foods
Liquid egg
Salmonella and spoilage bacteria
Honey
Spoilage yeast
Meat surfaces (steam, hot water)
E. coli O157: H7, Salmonella, Campylobacter

## Slide 15
Milk Pasteurization
Time/Temperature Combinations
High Temperature Short Time (HTST) 15 sec @ 72oC
Low Temperature Long Time (LTLT) 30 min at 63oC
These pasteurization time/temperatures are considered to be equivalent.
Heat treatments are established on the basis of safety first (elimination of pathogens) and spoilage (extension of shelf life) second.

## Slide 16: Plate heat exchanger

## Slide 17: 4. Effect on foods
Pasteurization is a relatively mild heat treatment and even when combined with other unit operations (for example irradiation and chilling there are only minor changes to the nutritional and sensory characteristics of most foods. However, the shelf life of pasteurized foods is usually only extended by a few days or weeks compared with many months with the more severe heat sterilization. Minimizing post processing contamination is essential to ensure an adequate shelf life.

## Slide 18: 4.1 Vitamin loss
In fruit juices, losses of vitamin C and carotene are minimized by deaeration. Changes to milk are confined to a 5% loss of serum proteins and small changes to the vitamin content
Vitamin losses during pasteurization of milk
Holder

## Slide 19
Heat processing using hot oils (Frying)

## Slide 20: Heat processing using hot oils (Frying)
Frying is a unit operation which is mainly used to alter the eating quality of a food. A secondary consideration is the preservative effect that results from thermal destruction of micro-organisms and enzymes, and a reduction in water activity at the surface of the food (or throughout the food, if it is fried in thin slices).
The shelf life of fried foods is mostly determined by the moisture content after frying

## Slide 21
Foods that are more thoroughly dried by frying, for example potato crisps (potato chips in the USA), maize and other potato snackfoods, have a shelf life of up to 12 months at ambient temperature.
The quality is maintained by adequate barrier properties of packaging materials and correct storage conditions.

## Slide 22: 5.1 Theory
When food is placed in hot oil, the surface temperature rises rapidly and water is vaporised as steam. The surface then begins to dry out in a similar way to that described during baking and roasting.
The plane of evaporation moves inside the food, and a crust is formed. The surface temperature of the food then rises to that of the hot oil, and the internal temperature rises more slowly towards 100 ºC.
The rate of heat transfer is controlled by the temperature difference between the oil and the food and by the surface heat transfer coefficient. The rate of heat penetration into the food is controlled by the thermal conductivity of the food

## Slide 23
During frying, both water and water vapour are removed from the larger capillaries first, and replaced by hot oil.
Moisture moves from the surface of the food through a boundary film of oil, the thickness of which controls the rate of heat and mass transfer.

## Slide 24: The time taken for food to be completely fried depends on:
• the type of food
• the temperature of the oil
• the method of frying (shallow or deep-fat frying)
• the thickness of the food
• the required change in eating quality

## Slide 25
The temperature used for frying is determined mostly by economic considerations and the requirements of the product.
At high temperatures (180–200 ºC), processing times are reduced and production rates are therefore increased. However, high temperatures also cause accelerated deterioration of the oil and formation of free fatty acids, which alter the viscosity, flavour and colour of the oil and promote foaming. This increases the frequency with which oil must be changed and hence increases costs.

## Slide 26
There are two main methods of commercial frying which are distinguished by the method of heat transfer involved: these are
1- shallow frying
2- deep-fat frying.
Fig.1. Shallow frying
Fig.2. deep-fat-frying

## Slide 27: 5.2 Shallow (or contact) frying
Definition:
Shallow frying is the cooking of food in a small quantity of pre-heated fat or oil in a shallow pan or on a flat surface
This method is most suited to foods which have a large surface-area-to-volume ratio for example bacon slices, eggs, burgers and other types of patties). Heat is transferred to the food mostly by conduction from the hot surface of the pan through a thin layer of oil

## Slide 28: Heat and mass transfer in (a) shallow frying and (b) deep fat frying.

## Slide 29: 5.3 Deep-fat frying
Here heat transfer is a combination of convection within the hot oil and conduction to the interior of the food. All surfaces of the food receive a similar heat treatment, to produce a uniform color and appearance.
Deep-fat frying is suitable for foods of all shapes, but irregularly shaped food or pieces with a greater surface: mass ratio tend to absorb and entrain a greater volume of oil when it is removed from the fryer

## Slide 30: 5.4 Equipment
Shallow-frying equipment consists of a heated metal surface, covered in a thin layer of oil. Commercially, continuous deep-fat fryers are more important.
In batch operation the food is suspended in a bath of hot oil and retained for the required degree of frying, often assessed by changes in surface color.

## Slide 31: Continuous deep-fat frier.

## Slide 32: Different conveyor arrangements: (a) delicate non-buoyant products (for example fish sticks); (b) breadcrumb-coated products; (c) dry buoyant bulk products (for example half-product snacks); (d) dual purpose (for example nuts and snacks).

## Slide 33: 5.5 Effect on foods
Frying is an unusual unit operation in that the product of one food process (cooking oil) is used as the heat transfer medium in another. The effect of frying on foods therefore involves both the effect on the oil, which in turn influences the quality of the food, and the direct effect of heat on the fried product.

## Slide 34: 5.5.1 Effect of heat on oil
Prolonged heating of oils at the high temperatures used in frying, in the presence of moisture and oxygen released from foods, causes oxidation of the oil to form a range of volatile carbonyls, hydroxy acids, keto acids and epoxy acids. These cause unpleasant flavours and darkening of the oil.
The various breakdown products are classified as volatile decomposition products (VDP) and non-volatile decomposition products (NVDP).

## Slide 35
VDPs have a lower molecular weight than the oil and are lost in vapour from the frier. Analysis of the vapour has indicated up to 220 different components, which form the smoke and odour of frying. However, these components are also present in the oil and contribute to the flavour of the fried product.
NVDPs are formed by oxidation and polymerisation of the oil and form sediments on the sides and at the base of the frier. Polymerisation in the absence of oxygen produces cyclic compounds and high-molecular-weight polymers, which increase the viscosity of the oil. This lowers the surface heat transfer coefficient during frying and increases the amount of oil entrained by the food.

## Slide 36
Oil absorption may depend on:
surface/volume of foods
oil temperature
crust composition
moisture content of food
thermal history of oil

## Slide 37: 5.5.2 Effect of heat on fried foods
The main purpose of frying is the development of characteristic colours, flavours and aromas in the crust of fried foods. These eating qualities are developed by a combination of Maillard reactions and compounds absorbed from the oil. The main factors that control the changes to colour and flavour in a given food are therefore:
the type of oil used for frying
the age and thermal history of the oil

## Slide 38
the interfacial tension between the oil and the product
the temperature and time of frying
the size, moisture content and surface characteristics of the food
post-frying treatments

## Slide 39
Each of these factors, together with any pre-treatments, such as blanching or partial drying, also influences the amount of oil entrained within the food.
Where fried foods form a large part of the diet, excess fat consumption can be an important source of ill-health, and is a key contributor to obesity, coronary heart disease and perhaps some types of cancer. These risks and consumer trends towards lower fat products is creating pressure on processors to alter processing conditions to reduce the amount of oil absorbed or entrained in their products.

## Slide 40
The texture of fried foods is produced by changes to proteins, fats and polymeric carbohydrates which are similar to those produced by baking. Changes to protein quality occur as a result of Maillard reactions with amino acids in the crust.
The fat content of the food increases owing to oil absorption and entrainment, but the nutritional significance of this is difficult to determine as it varies according to a number of factors including the type and thermal history of the oil, and the amount entrained in the food.

## Slide 41
Effect of frying on nutritional value depends on type of process.
• High oil temperatures produce rapid crust formation & seal the food surface.
Few losses during storage, e.g.
• 17% loss of available lysine in fried fish; this increased to 25% when thermally damaged oil was used.
• Shallow-fried liver lost 15% thiamin.
• Vitamin C losses in fried potatoes are lower than in boiling
nutritional value

## Slide 42: Vacuum Frying
Advantages of vacuum frying
• Can reduce oil content in the fried product.
• Can preserve natural color & flavors of the product due to the low temperature & oxygen
content during the process.
• Has less adverse effects on oil quality

## Slide 43
How its made pringles